## Slide 1: Word Size and Data Types
Embedded Software Essentials
C2M1V2

## Slide 2
Architecture designed to implement assembly instructions
Complex Instruction Set Computer (CISC)
Reduced Instruction Set Computer (RISC)
Advanced RISC Machine (ARM)
Instruction_a
Instruction_b
Instruction_c
Instruction_d
…
Flash
Result
Arithmetic Logical
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction_c
CPU
Architecture [S1]
Instruction
Register

## Slide 3
Instruction – Fundamental unit of work or operation
  Arithmetic
  Logical
  Program Flow Control
  Load/Store
Word – fundamental operand size for each operation
Units of Operation [S2]
Example: 32-bit Machines are built to do 32-bit math most optimally
Inside a CPU
Result
Arithmetic Logical
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction_c
Instruction
Register

## Slide 4
Units of Operation [S3]
N-bit Data Bus (internal)
N-bit Registers
N-bit ALU
CPU operand size = data size of registers
CPU N-bit architecture
General Purpose Registers in CPU will be size of the Word
Cortex-M Processors has General and Special Purpose CPU Core registers
  R0-R12 General Purpose
  R13-R15 Reserved Role
  Program Status Registers
  Exception Mask Registers
  Control Register
ARM 32-bit Word = 32-bit registers
Core CPU Registers
N-bits wide
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0497a/CHDBIBGJ.html

## Slide 5: Instruction Sizes [S4]
Instruction size can vary
  ARM Instruction Set ARMv6-M  16-Bit and 32-Bit
  Thumb-2 Instruction Set  16-Bit
000104c8 <main>:
104c8: b5b0 push {r4, r5, r7, lr}
104ca: b096 sub sp, #88
104cc: af00 add r7, sp, #0
104ce: f241 0330 movw r3, #4144
104d2: f2c0 0302 movt r3, #2
Instruction Address
Machine Code
Assembly Code
32-Bit
Instructions
16-Bit
Instructions
Example Output with Machine Code and Assembly Code

## Slide 6
Units of Operation [S5]
N-bit Registers
N-bit ALU
CPU N-bit architecture
There are a lot of Busses in a Microcontroller
  Internal System Busses
    Example: ARM AHB
  External Peripheral Busses
    Example: ARM APB
Bus is at least the size of the instruction
M-bit External Peripheral Data Bus or Crossbar
GPIO
Timer
Analog
UART
N-bit Internal Data Bus
Bus Fabric
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0497a/CHDBIBGJ.html

## Slide 7: C-Programming Types [S6]
Sizes of C data types are ambiguous and vary between architectures
C-Standard Specifies a minimum each variable can be
Type
Size
Value Range (min)
signed char
int8_t
At least 16-bits
At least 8-bits
signed short int
int16_t
At least 32-bits
signed long int
int32_t
[-215, +215 – 1]
[-215, +215 – 1]
[-27, +27 – 1]
At least 32-bits
unsigned char
uint8_t
At least 8-bits
[0, +28 – 1]
unsigned short int
uint16_t
At least 16-bits
[0, +216 – 1]
[0, +232 – 1]
unsigned long int
uint32_t

## Slide 8: Standard Integer Sizes[S7]
Variable length Types can cause portability issues
Explicitly defined types that specify storage and sign
  Provide exact size, fast size, and minimum size
Defined in the stdint.h header file
int8_t
int16_t
int32_t
int64_t
uint8_t
uint16_t
uint32_t
uint64_t
Exactly 8-bits
Exactly 16-bits
Exactly 32-bits
Exactly 64-bits
Exactly 8-bits
Exactly 16-bits
Exactly 32-bits
Exactly 64-bits

## Slide 9: Standard Integer Sizes[S8]
Explicitly defined types that specify exact size and sign
  U = Unsigned
  Int = Integer type
  _t = type
#ifndef __STDINT_H__
#define __STDINT_H__
/* 8-bit signed/unsigned Integers */
typedef signed char int8_t;
typedef unsigned char uint8_t;
/* 16-bit signed/unsigned Integers */
typedef signed short int int16_t;
typedef unsigned short int uint16_t;
/* 32-bit signed/unsigned Integers */
typedef signed long int int32_t;
typedef unsigned long int uint32_t;
/* 64-bit signed/unsigned Integers */
typedef signed long long int int64_t;
typedef unsigned long long int uint64_t;
#endif /* __STDINT_H__ */
uint16_t
unsigned
integer
16-bits
int32_t
signed
integer
32-bits
uint8_t var1;
int32_t var3 = -100;

## Slide 10: Standard Integer Sizes [S9]
You need a data size that allows for the fastest access while having at least N bits  Fast Types
  Typically rounds up to word size
    Most optimum size for operations
You need the smallest data size that has a minimum size N bits
 Least Types
int_fast8_t var1;
uint_least16_t var2 = 12;
int_fast8_t
int_fast16_t
int_fast32_t
int_fast64_t
uint_fast8_t
uint_fast16_t
uint_fast32_t
uint_fast64_t
int_least8_t
int_least16_t
int_least32_t
int_least64_t
uint_least8_t
uint_least16_t
uint_least32_t
uint_least64_t

## Slide 11: Typedef [S10]
Typedef keyword allows programmer to create own types (like an alias)
  Can apply to standard types or derived types
#ifndef __STDINT_H__
#define __STDINT_H__
/* 8-bit signed/unsigned Integers */
typedef signed char int8_t;
typedef unsigned char uint8_t;
/* 16-bit signed/unsigned Integers */
typedef signed short int int16_t;
typedef unsigned short int uint16_t;
/* 32-bit signed/unsigned Integers */
typedef signed long int int32_t;
typedef unsigned long int uint32_t;
/* 64-bit signed/unsigned Integers */
typedef signed long long int int64_t;
typedef unsigned long long int uint64_t;
#endif /* __STDINT_H__ */
typedef enum Color {
COLOR_BLUE = 0,
COLOR_RED = 1,
COLOR_GREEN = 2,
} Color_t;
typedef struct Data {
int32_t temperature;
unt32_t date;
unt32_t time;
} Data_t;