## Slide 1: Interacting With Memory
Embedded Software Essentials
C2M1V4

## Slide 2: Microcontroller Memory [S1]
Memory is used during every single instruction
Microcontroller
Flash
CPU
Peripherals
SRAM
Generalized ARM CPU
Result
Arithmetic Logical
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction
PSR
Mask Registers
Control
Special Function
Registers

## Slide 3: Embedded Memory [S2]
Microcontroller
GPIO
Code Memory
(Flash)
CPU
Peripherals
Data Memory
(SRAM)
Memories of an Embedded Systems
  Code Memory (Flash)
  Data Memory (SRAM)
  Register Memory
The CPU and peripherals contain register memory
  CPU Registers
    General Purpose
    Special Purpose
  General Peripheral Registers
Registers
Registers
Registers

## Slide 4: Core CPU Registers [S3]
CPU Registers have unique identifiers
  r0-r15, sp, pc, lr
  apsr, ipsr, epsr
  primask, faultmask, control, etc
CPU
Bus Interface
SRAM
Store from
R10
Load into
R4
Example Assembly Code

## Slide 5: Load-Store Architecture [S4]
CPU Register memory is small
  16 Registers (R0-R12, SP, PC, LR)
  5 Special Function Registers
All processing occurs in CPU
CPU Register data constantly changes
  Data is loaded in from memory
  Results are stored back to memory
SRAM
Flash
Result
Arithmetic Logical
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction
CPU
Instruction Fetch
Data Load/Store

## Slide 6: Read-Modify-Write [S5]
Read: Data is loaded into CPU
Modify: Data is Operated on
Write: Result is stored back
Compiler tries to reduce number of loads and stores for execution efficiency
CPU
Bus Interface
SRAM
Store from
R10
Load into
R4
Optimization
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0497a/CHDBIBGJ.html

## Slide 7: Peripheral Registers [S6]
Peripheral register require some contents (bit-fields) to be preserved
Use bit manipulation to change certain bits of a register (not all contents)
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
*ptr |= 0x10;
Set 4th bit without changing other bits:
*ptr &= ~(0x10);
Clear 4th bit without changing other bits:
uint8_t * ptr = (uint8_t *) 0x1000;

## Slide 8: Bit-Banded Regions [S7a]
Microcontroller
Flash
CPU
Peripherals
SRAM
Reduces Read-Modify-Write overhead!
Code
Data
Peripherals
System
Memory Map
Bit-Banded Regions allow programmer to perform bit-level loads and stores
Bit-Banded operations are atomic
  Handled in hardware
  No CPU Load/Store

## Slide 9: Bit-Banded Regions [S7b]
Bit-Banded Regions allow programmer to perform bit-level loads and stores
Bit-Banded operations are atomic
  Handled in hardware
  No CPU Load/Store
Code
Data
Peripherals
System
Memory Map
Reduces Read-Modify-Write overhead!
(Unused)
Bit-Banded Region
SRAM
(Unused)
Data Region
0x20000000
0x2FFFFFFF
0x23FFFFFF
0x22000000
0x20100000

## Slide 10: Data/Instructions Busses [S8a]
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Simplistic model shows only 1 bus interface to all components of the microcontroller

## Slide 11: Microcontroller Busses [S8b]
Microcontroller
Cortex-M
SRAM Memory
Flash Memory
Flash
Controller
AHB Flash I-code Bus
AHB Flash
D-code Bus
High-Speed Peripheral
High-Speed Peripheral
High-Speed Peripheral
AHB System Bus
Bridge
Peripherals
Peripherals
Peripherals
APB
Peripheral
Bus
PPB (Internal)
High-Speed Peripheral
High-Speed Peripheral
Internal Private Peripherals
PPB (External)
Debugger

## Slide 12: Private Bus Interfaces [S9]
Microcontroller
Cortex-M
SRAM Memory
Flash Memory
Flash
Controller
AHB Flash I-code Bus
AHB Flash
D-code Bus
High-Speed Peripheral
AHB System
Bus
Bridge
Peripherals
Peripherals
Peripherals
APB
Peripheral
Bus
PPB (Internal)
Internal Private Peripherals
PPB (External)
Debugger
AMBA High-Performance Bus (AHB)
  Fast/High-Bandwidth Interfaces
Private Cortex-M4 Busses
  Internal Private Peripherals Bus (PPB)
    NVIC, SCS, MPU
  External Private Peripherals Bus (PPB)
    External Debugging

## Slide 13: Code and Data Busses [S10]
Microcontroller
Cortex-M
SRAM Memory
Flash Memory
Flash
Controller
AHB Flash I-code Bus
AHB Flash
D-code Bus
High-Speed Peripheral
AHB System
Bus
Bridge
Peripherals
Peripherals
Peripherals
APB
Peripheral
Bus
PPB (Internal)
Internal Private Peripherals
PPB (External)
Debugger
AHB External Core AHB busses
  System Bus (AHB-Lite)
    SRAM
    High Speed Peripherals
    Peripheral Bridge
  Flash Bus
    I-Code Bus
    D-Code Bus
Flash Busses allow for fetching of Code and Flash Data simultaneously

## Slide 14: Peripheral Bus [S11]
Microcontroller
Cortex-M
SRAM Memory
Flash Memory
Flash
Controller
AHB Flash I-code Bus
AHB Flash
D-code Bus
High-Speed Peripheral
AHB System
Bus
Bridge
Peripherals
Peripherals
Peripherals
APB
Peripheral
Bus
PPB (Internal)
Internal Private Peripherals
PPB (External)
Debugger
Advanced Peripheral Bus (APB)
  Low Bandwidth Bus
  Connected to CPU via Bridge to System Bus
Interfaces with Low Bandwidth
  Communications
    UART
    SPI
    I2C
  Timers
  ADC