## Slide 1: Endianness
Embedded Software Essentials
C2M1V6

## Slide 2: Memory [S1]
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Memory storage interacting with the CPU
  Code Memory
  Data Memory
  Registers (Peripherals)
Memory interfaces to CPU through Busses
Load-Store architecture requires operations to occur in CPU
  Data get loaded into CPU
  Data is operated on
  Data is stored back to memory
Registers
Registers
Registers

## Slide 3: Data Order [S2]
Each address stores 1 Byte
Half-Words store 2 Bytes
Words store 4 Bytes
Which location stores the MSB?
Which location stores the LSB?
Memory
word
half-word
byte
0x100
0x108
0x104
0x101
0x102
0x103
0x105
0x106
0x107
0x109
0x110
0x111

## Slide 4: Endianness [S3]
MSB
uint32_t var = 0xABCD1234;
Endianness = How data is represented
Byte-order in memory!
LSB
4-Bytes
Can express data order in two different ways
Little Endian
Big Endian
Endianness only relevant for multi-byte data!

## Slide 5: Endianness [S4]
uint32_t var = 0xABCD1234;
AB
CD
12
34
Memory
Big Endian:
Store MSB at smallest address
0x100
0x101
0x102
0x103
Endianness = How data is represented
Byte-order in memory!

## Slide 6: Endianness [S5]
34
12
CD
AB
Memory
Little Endian:
Store LSB at smallest address
uint32_t var = 0xABCD1234;
AB
CD
12
34
Memory
Big Endian:
Store MSB at smallest address
0x100
0x101
0x102
0x103
0x100
0x101
0x102
0x103
Endianness = How data is represented
Byte-order in memory!

## Slide 7: Types and Endianness [S6]
Endianness does not affect order of elements Arrays or Structures
0x34
0x12
0x67
0x45
0xAB
0x89
0xEF
0xCD
Little Endian Memory
array[0]
0x108
0x104
0x101
0x102
0x103
0x105
0x106
0x107
0x109
0x110
0x111
uint16_t array[4] = { 0x1234,
0x4567,
0x89AB,
0xCDEF };
2-Bytes
0x100
array[2]
array[1]
array[3]

## Slide 8: Endianness Configuration [S7]
Endianness is Configurable on many modern platforms
ARM Cortex-M allows for configuration of Data Memory Endianness
Code Memory is set to little endian
Boring Slide. This would be good just to do text

## Slide 9: Endianness Configuration [S8]
Application Interrupt and Reset Control Register (AIRCR)
  Allows for reconfiguration of Data Memory Endianness
Bit 15 of AIRCR Register
  0 = Little Endian
  1 = Big Endian
Changing Endianness requires a reset
AIRCR Register Bit Fields
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/Cihehdge.html

## Slide 10: Endianness Trouble [S9]
Endianness must be accounted for
  Supporting Multiple platforms/Architectures with the same code base
  Connecting multiple systems together
Microcontroller
GPIO
Flash
CPU-1
Peripheral
SRAM
UART
Microcontroller
GPIO
Flash
CPU-2
Peripheral
SRAM
UART
Same code, different endianness, may transmit byte order opposite
Platform 1, Architecture 1
Platform 2, Architecture 2

## Slide 11: Byte-Swapping [S10a]
/* Switches endianness of variable pointed by ptr */
void byte_swap32(uint32_t * ptr){
uint8_t i, temp_byte;
for (i = 0; i < 2; i++){
temp_byte = *((uint8_t*)ptr + (3-i));
*((uint8_t*)ptr + (3-i)) = *((uint8_t*)ptr + i)
*((uint8_t*)ptr + i) = temp_byte;
}
}
/* Assume little endian */
void main(){
uint32_t var = 0xABCD1234;
uint32_t * ptr = &var;
byte_swap32(ptr);
while (1);
}
Memory
0x00
0x01
0x02
0x03
AB
CD
12
34
Memory
0x00
0x01
0x02
0x03
Before
After

## Slide 12: Byte-Swapping [S10b]
34
12
CD
AB
Memory
0x00
0x01
0x02
0x03
AB
CD
12
34
Memory
0x00
0x01
0x02
0x03
/* Switches endianness of variable pointed by ptr */
void byte_swap32(uint32_t * ptr){
uint8_t i, temp_byte;
for (i = 0; i < 2; i++){
temp_byte = *((uint8_t*)ptr + (3-i));
*((uint8_t*)ptr + (3-i)) = *((uint8_t*)ptr + i)
*((uint8_t*)ptr + i) = temp_byte;
}
}
/* Assume little endian */
void main(){
uint32_t var = 0xABCD1234;
uint32_t * ptr = &var;
byte_swap32(ptr);
while (1);
}
Before
After

## Slide 13: Unused Slides

## Slide 14: Portability with Endianness [S9a]
In little endian architecture...
24
F9
0C
12
...
33
07
0x4000
0xF90C
0x4001
0x4002
0x4003
0xF90D
array
ptr
...
0x2412
0x2413
0x2414
0x2415
Invalid
section
33
07
0x4000
0x4001
Dereference at valid address
/* Program depends on LE architecture. */
void main(){
uint16_t array[] = {0xF924, 0x120C, 0};
uint16_t * ptr = (uint16_t*) ((array[0] & 0xFF00) | (array[1] & 0xFF));
array[2] = *ptr;
// Rest of code...
}

## Slide 15: Portability with Endianness [S9b]
F9
24
12
0C
...
07
33
0x4000
0xF90C
0x4001
0x4002
0x4003
0xF90D
array
ptr
...
0x2412
0x2413
0x2414
0x2415
Invalid
section
07
33
0x4000
0x4001
/* Program depends on LE architecture. */
void main(){
uint16_t array[] = {0xF924, 0x120C, 0};
uint16_t * ptr = (uint32_t) ((array[0] & 0xFF00) | (array[1] & 0xFF));
array[2] = *ptr;
// Rest of code...
}
Dereferenced at invalid address!
In big endian architecture...