## Slide 1: Registers
Embedded Software Essentials
C2M1V8

## Slide 2: Embedded System Memories [S1]
Memories of an Embedded Systems
  Code Memory (Flash)
  Data Memory (SRAM)
  Register Memory (internal to chip)
  External Memory (if applicable)
Compilation tracks and maps memory from a program into segments
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Specified in the Linker File

## Slide 3: Registers [S1a]
Bit 0
Bit 1
Bit 2
Bit 3
Bit 4
Bit 5
Bit 6
Bit 7
8-bit Register
(MSB)
(LSB)
Registers store temporary data
  Can Be Read/Write or Read-Only
Typically divided into multiple bit fields

## Slide 4: Registers [S1b]
Bit 0
Bit 1
Bit 2
Bit 3
Bit 4
Bit 5
Bit 6
Bit 7
8-bit Register
(MSB)
(LSB)
Registers store temporary data
  Can Be Read/Write or Read-Only
Typically divided into multiple bit fields
Core CPU Registers
Code
Data
Peripherals
System
Device
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Memory Map
0x00000000
0xFFFFFFFF
Addresses

## Slide 5: Memory Map [S2]
Memory Map: Provides a memory address to physical device mapping within an address space for use in programming
Address Space (Ranges for each device)
Mapped Components (Memory, Peripherals, System Config, etc.)
Notes: http://infocenter.arm.com/help/topic/com.arm.doc.dui0203h/DUI0203H_rvct_developer_guide.pdf

## Slide 6: Embedded Memory [S3]
Compilation tracks and maps memory from program code and program data into segments
  Code Segment (Flash)
  Data Segment (SRAM)
Memory allocation is application dependent
  Exact address allocation changes at every compile
Specified in the Linker File
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
DATA (RW) : origin = 0x20000000, length = 0x00010000
}

## Slide 7: Register Memory [S4a]
Registers from Peripherals, System and Vendor specific regions have immutable addresses
Typical Register Memories
  Internal Core CPU
  Internal Private Peripherals
  External Private Peripherals
  General Peripheral Memory
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Examples:
CPU Core Register Identifiers: r0-r16
Timer A0 Control Register Address: 0x40000000

## Slide 8
Core CPU Registers [S4b]
Cortex-M CPU Core registers
  r0-r15 General Purpose
  r13-r15 Special Role (lr, sp, pc)
  Program Status Registers
  Exception Mask Registers
  Control Register
General Purpose Registers
  Used on every clock cycle
  Always updating
Core CPU Registers
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0497a/CHDBIBGJ.html

## Slide 9
Core CPU Registers [S5]
Cortex-M CPU Special Function Registers
  Program Status Registers
    APSR
    IPSR
    EPSR
  Exception Mask Registers
    PRIMASK
    FAULTMASK
    BASEPRI
  Control Register
MRS r1, BASEPRI
MSR FAULTMASK, r0
Not part of the memory map. Needs special instructions to read/write
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0497a/CHDBIBGJ.html

## Slide 10: Cortex-M4 Program Status Registers [S6a]
PSR
The Program Status Register (PSR) captures the current CPU and program application state.

## Slide 11: Cortex-M4 Program Status Registers [S6b]
The PSR combines the APSR, EPSR, IPSR
PSR
APSR
EPSR
IPSR
The Program Status Register (PSR) captures the current CPU and program application state.
These status registers are mutually exclusive bit fields in the 32-bit PSR.
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 12: Cortex-M4 Program Status Registers [S7]
PSR
APSR
EPSR
IPSR
Reserved
N
31
27
28
29
30
Z
C
V
Q
Status Flags
N = Negative Flag
Z = Zero Flag
C = Carry Flag
V = Overflow Flag
Q = Saturation Flag
Was last result negative?
Was last result zero?
Did last result have a carry?
Did last result have an overflow?
Did last result saturate?
26:0
The Application Program Status Register (APSR) contains current state of condition flags from previous instruction execution

## Slide 13: Cortex-M4 Program Status Registers [S8]
PSR
APSR
EPSR
IPSR
8:0
31:9
Number of Current Exception
Reserved
Exception_NUM
Exception Numbers:
  0 = Reset
  1 = Non-Maskable Interrupt (NMI)
  2 = Hard Fault
  3 = Memory Management Fault
  …
  16 = IRQ0
  17 = IRQ1
  …
  N+15 = IRQ(n-1)
Reserved
The Interrupt Program Status Register (IPSR) contains the exception type number of the current ISR.

## Slide 14: Exception Mask Registers [S9a]
PRIMASK
  Prevents activation of all exceptions with configurable priority (If set to 1)
FAULTMASK
  Prevents activation of all exceptions with configurable priority EXCEPT the Non-Maskable Interrupt (NMI) (If set to 1)
BASEPRI
  Defines minimum priority for exception processing
Reserved
0
31:1
PRIMASK
Reserved
0
31:1
FAULTMASK
Reserved
7:0
31:8
BASEPRI

## Slide 15: Control Register [S9b]
FPCA – Floating Point State Active
  0 = No Floating Point Context Active
  1 = Floating Point Context Active
SPSEL – Selects Current Stack Pointer
  0 = MSP – Main Stack Pointer
  1 = PSP – Process Stack Pointer
nPRIV – Defines Privilege Level
  0 = Privileged
  1 = Unprivileged
Reserved
0
31:3
nPRIV
1
FPCA
2
SPSEL
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 16: Private Peripherals [S10]
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
Reserved
MPU
Processor Debug Control
FPU
System Control Block (SCB)
SysTick Timer
Misc system control registers
NVIC
System Control Space (SCS)
Reserved
FPB
DWT
ITM (ETM)
Reserved
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 17: General Peripherals [S11a]
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
(Reserved)
SRAM
SRAM Bit Band Alias Region
(Reserved)
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Peripheral Zone Memory Map
Sram Zone Memory Map
512 KB
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 18: General Peripherals [S11b]
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
(Reserved)
SRAM
SRAM Bit Band Alias Region
(Reserved)
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Peripheral Zone Memory Map
SRAM Zone Memory Map
4KB
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
Peripheral Devices
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 19: Timer A0 Peripheral [S12]
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
Timer_A0 Control
Timer_A0 CAPCOM Control 0
Timer_A0 Counter
Timer_A0 Interrupt Vector
Timer_A0 Expansion 0
Timer_A0 CAPCOM Control 1
Timer_A0 CAPCOM Control 2
Timer_A0 CAPCOM Control 3
Timer_A0 CAPCOM Control 4
Timer_A0 CAPCOM 0
Timer_A0 CAPCOM 1
Timer_A0 CAPCOM 2
Timer_A0 CAPCOM 3
Timer_A0 CAPCOM 4
Timer_A0 Registers
0x40000000
0x40000002
0x40000004
0x40000006
0x40000008
0x4000000A
0x40000010
0x40000012
0x40000014
0x40000016
0x40000018
0x4000001A
0x4000002E
0x40000020
Peripheral Devices
Peripheral Zone
Memory Map
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
4KB
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 20: Timer A0 Control Register [S13a]
Timer_A0 Control Register
TAIFG
0
TAIE
1
TACLR
2
Reserved
3
MC
5
4
ID
7
6
TASSEL
9
8
Reserved
15:10
Bit fields are variables with predefined widths (i.e. non-standard sizes) within the register
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 21: Timer A0 Control Register [S13b]
Timer_A0 Control Register
TAIFG
0
TAIE
1
TACLR
2
Reserved
3
MC
5
4
ID
7
6
TASSEL
9
8
Reserved
15:10
Bit fields are variables with predefined widths (i.e. non-standard sizes) within the register
TASSEL
ID
MC
TACLR
TAIE
TAIFG
= Select input clock source for Timer_A0
= Select input clock divider for Timer_A0
= Select count-mode for Timer_A0
= Resets Timer_A0
= Enable Timer_A0 interrupt
= Timer_A0 interrupt flag
Bit fields of Timer_A0 Control Register
Bit Fields help represent operations/status/configurations.
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 22: Timer A0 Control Register [S13c]
Timer_A0 Control Register
TAIFG
0
TAIE
1
TACLR
2
Reserved
3
MC
5
4
ID
7
6
TASSEL
9
8
Reserved
15:10
Bits 15:10 and 3 are reserved
Reserved bits can be:
Unused
Reserved for advanced sub-family models
For internal use only
TASSEL
ID
MC
TACLR
TAIE
TAIFG
= Select input clock source for Timer_A0
= Select input clock divider for Timer_A0
= Select count-mode for Timer_A0
= Resets Timer_A0
= Enable Timer_A0 interrupt
= Timer_A0 interrupt flag
Bit fields of Timer_A0 Control Register
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 23: Timer A0 Control Pointer [S14]
16-Bit Register (Address = 0x40000000)
Configure for:
  TASSEL = 2 = 0b10
  TAIE = 1 = 0b1
Timer_A0 Control Register
TAIFG
0
TAIE
1
TACLR
2
Reserved
3
MC
5
4
ID
7
6
TASSEL
9
8
Reserved
15:10
volatile uint16_t * ta0_ctrl = (uint16_t*)0x40000000;
*ta0_ctrl = 0x0202;
0b10
0b1
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 24: Unused Slides

## Slide 25: Memory Map [S1.3.5.a]
SRAM
Code
Reserved
Memory
General Purpose and Special Registers
Peripherals
Reserved
Interrupt Vector Table
0x00000000
0xFFFFFFFF
0xE0100000
0xD0000000
0x30000000
0x20000000
0xE00FFFFF
0x3EFFFFFF
0x20000000
Process of dividing the Address Space into logical sections

## Slide 26: Memory Map [S1.3.5.b]
e.g. 0x00000000-0x09FFFFFF range mapped to flash
Flash
System Memory
0x00000000
0x09FFFFFF
0x1E0FFFFF
0x0A000000
SRAM
Code
Reserved
Memory
General Purpose and Special Registers
Peripherals
Reserved
Interrupt Vector Table
0x00000000
0xFFFFFFFF
0xE0100000
0xD0000000
0x30000000
0x20000000
0xE00FFFFF
0x3EFFFFFF
0x20000000
Address ranges are mapped to particular functions
Process of dividing the Address Space into logical sections

## Slide 27: Memory Map [S1.3.5.c]
e.g. 0x00000000-0x09FFFFFF range mapped to flash
Addresses act as a physical/virtual access of a memory location
SRAM
Code
Reserved
Memory
General Purpose and Special Registers
Peripherals
Reserved
Interrupt Vector Table
0x00000000
0xFFFFFFFF
0xE0100000
0xD0000000
0x30000000
0x20000000
0xE00FFFFF
0x3EFFFFFF
0x20000000
Address ranges are mapped to particular functions
Process of dividing the Address Space into logical sections
Flash
System Memory
0x00000000
0x09FFFFFF
0x1E0FFFFF
0x0A000000

## Slide 28: Memory Map [S1.3.5.d]
e.g. 0x00000000-0x09FFFFFF range mapped to flash
Addresses act as a physical/virtual access of a memory location
SRAM
Code
Reserved
Memory
General Purpose and Special Registers
Peripherals
Reserved
Interrupt Vector Table
0x00000000
0xFFFFFFFF
0xE0100000
0xD0000000
0x30000000
0x20000000
0xE00FFFFF
0x3EFFFFFF
0x20000000
Address ranges are mapped to particular functions
Process of dividing the Address Space into logical sections
Typically includes: Flash, SRAM, Peripherals, Debug,
General Purpose and Special Registers
Flash
System Memory
0x00000000
0x09FFFFFF
0x1E0FFFFF
0x0A000000
Notes: @Alex Do memory maps only refer to peripherals? Can memory maps refer to actual raw memory?

## Slide 29: Types of Registers [S1.3.6.b]
R0-R12
R13-R15
CPU Registers
General-Purpose Registers
CPU-Special Registers
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
SCB
NVIC
xPSR
CONTROL
Special Registers
System Control Block
Nested Vector Interrupt Controller
Program Status Registers
Processor’s control
Peripheral n
Data Register
Peripheral n
Control Register
Peripherals
Notes: Expand to 3 slides, with brief explanations for each

## Slide 30: Address Space [S1.3.5.3]
The address space is the range of valid addresses in memory that a program/process can access.
Physical Address Space
Process 3
Code
Process 2
Process 1
0x00000
0xFFFFF
Virtual Address Spaces
Address space 1
0x00000
0xFFFFF
Address space 2
0x00000
0xFFFFF
Address space 3
0x00000
0xFFFFF
Peripherals located (i.e. mapped) to address space of physical memory (memory space) are called
Memory Mapped Peripherals
(or more commonly memory mapped I/O).
Easy for programmer to interface address space due to bus decision making.
However, different address spaces require different read/write mechanisms.
Notes: Transition for Address Space Figure?

## Slide 31: I/O Blocks and Peripheral Limitations [S1.3.5.4]
Typical size of address spaces are 4kB, though can be larger.
Because of memory mapped I/O, peripherals are therefore limited by size of address space.
4 kB Address Space for
Memory Mapped I/O
0x00000000
Peripheral 1
Data Register
Peripheral 1
Control Register
Peripheral 2
Data Register
Peripheral 2
Control Register
0x000000FF
Notes: I wanted to talk more about ARM memory, but not sure what to cover on it. Already talked about memory maps and address spaces; and as for registers, that should be talked about in next section?

## Slide 32: Types of Memory [S1.3.3.1a]
Read/write speed fast
Memory
Volatile
memory
Non-volatile
memory
Flash
RAM
Reading/writing to memory:
Expensive, Takes Time,
Architecture designed for memory cache hits
Read/write speed slow
Keeps data without power
Holds data & programs
Stores bootloader
Loses data
without power

## Slide 33: Stack Implementation [S4]
Show the different types of things that get put on stack (general)
Two types of routines

## Slide 34: CPU Registers [S6]

## Slide 35: Special Purpose Registers
APSR – Application Program Status Register
  NZCV = Flags that evaluate conditional execution
IPSR – Interrupt Program Status Register
EPSR – Execution Program Status Register
35
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0552a/CHDBIBGJ.html

## Slide 36: ARM Stack Calling Conventions
In ARM, the stack is a Full Descending Stack
  Starts at a High Address, and grows toward low addresses
LIFO – Last-in-First-Out
Used
Stack
Space
Unused
Stack
Space
High Address
Stack
Pointer
Low Address
Grows from high to low
Addresses

## Slide 37: Architecture Independence [S2]
Put a picture in of application code on top of hardware features or hardware specific code
Freedom Freescale – KL25z
SPI Peripheral Module
GPIO HW
SPI_Lib
SPI FW KL25z
Nordic_Lib
LED_Lib
UART_Lib
UART FW KL25z
UART Peripheral Module
Control_Lib
I/O

## Slide 38
Hardware
Operating System
Middleware
Applications
Libs
Drivers
Bootloader