## Slide 1: Register Definition Files
Embedded Software Essentials

## Slide 2: Embedded System Memories [S1]
Memories of an Embedded System
  Code Memory (Flash)
  Data Memory (SRAM)
  Register Memory (internal to chip)
  External Memory (if applicable)
Peripherals have special functionality each with a reserved spot in the memory map
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Addresses specified in a Register Definition File

## Slide 3: Peripheral Memory [S2]
Microcontrollers contain multiple Peripherals
  Private
    System Control Block (SCB)
    Nested Vector Interrupt Controller (NVIC)
  General
    UART / SPI / I2C
    Timers
    ADC
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
volatile uint16_t * ta0_ctrl = (uint16_t*)0x40000000;
*ta0_ctrl = 0x0202;
Access Peripherals with Pointers

## Slide 4: Register Definition File [S3]
Platform File that provides Interface to peripheral memory by specifying
  Address List for Peripherals
  Access Methods
  Defines for Bit Field and Bit Masks
Peripheral Access Methods are used to read/write data
  Direct Dereferencing of Memory
  Structure Overlays
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
Reserved
MPU
Processor Debug Control
FPU
SCB
SysTick Timer
Misc system control registers
NVIC
General
Peripherals
Private
Peripherals
Could Contain 1000’s of Registers!

## Slide 5: Directly Dereference Memory [S4]
Do not need a pointer variable to read/write to memory
volatile uint16_t * ta0_ctrl = (uint16_t*)0x40000000;
*ta0_ctrl = 0x0202;
Timer_A0 Control Register, Address = 0x40000000
TAIFG
0
TAIE
1
TACLR
2
Reserved
3
MC
5
4
ID
7
6
TASSEL
9
8
Reserved
15:10
(*(volatile uint16_t*)0x40000000)) = 0x0202;
Equivalent to Defining a Pointer!
Dereference!
Not Very Readable or Maintainable…

## Slide 6: Memory Access Macros [S5]
Use preprocessor to define an access method without using hardcoded values
/ * 8, 16, & 32 Bit Register Access Macros */
#define HWREG8(x) (*((volatile uint8_t *)(x)))
#define HWREG16(x) (*((volatile uint16_t *)(x)))
#define HWREG32(x) (*((volatile uint32_t *)(x)))
#define TA0CTL (HWREG16(0x40000000))
Pass in any address to access a Register
TA0CTL = 0x0202;
volatile uint16_t * ta0_ctrl = (uint16_t*)0x40000000;
*ta0_ctrl = 0x0202;
Example Use of Access Macro:

## Slide 7: Timer A0 Registers [S6]
Timer_A0 Control
Timer_A0 CAPCOM Control 0
Timer_A0 Counter
Timer_A0 Expansion 0
Timer_A0 Interrupt Vector
Timer_A0 CAPCOM Control 1
Timer_A0 CAPCOM Control 2
Timer_A0 CAPCOM Control 3
Timer_A0 CAPCOM Control 4
Timer_A0 CAPCOM 0
Timer_A0 CAPCOM 1
Timer_A0 CAPCOM 2
Timer_A0 CAPCOM 3
Timer_A0 CAPCOM 4
Timer_A0 Registers
0x40000000
0x40000002
0x40000004
0x40000006
0x40000008
0x4000000A
0x40000010
0x40000012
0x40000014
0x40000016
0x40000018
0x4000001A
0x40000020
0x4000002E
#define HWREG16(x) (*((volatile uint16_t *)(x)))
/ * Example Use of Access Macros */
#define TA0CTL (HWREG16(0x40000000))
#define TA0CCTL0 (HWREG16(0x40000002))
#define TA0CCTL1 (HWREG16(0x40000004))
#define TA0CCTL2 (HWREG16(0x40000006))
#define TA0CCTL3 (HWREG16(0x40000008))
#define TA0CCTL4 (HWREG16(0x4000000A))
#define TA0R (HWREG16(0x40000010))
#define TA0CCR0 (HWREG16(0x40000012))
#define TA0CCCR1 (HWREG16(0x40000014))
#define TA0CCCR2 (HWREG16(0x40000016))
#define TA0CCCR3 (HWREG16(0x40000018))
#define TA0CCCR4 (HWREG16(0x4000001A))
#define TA0EX0 (HWREG16(0x40000020))
#define TA0IV (HWREG16(0x4000002E))

## Slide 8: Timer A0 Registers [S6b]
#define TA0CTL (HWREG16(0x40000000))
#define TA0CCTL0 (HWREG16(0x40000002))
#define TA0CCTL1 (HWREG16(0x40000004))
#define TA0CCTL2 (HWREG16(0x40000006))
#define TA0CCTL3 (HWREG16(0x40000008))
#define TA0CCTL4 (HWREG16(0x4000000A))
#define TA0R (HWREG16(0x40000010))
/* More Register Macros Below */
#define TA0CTL (HWREG16(0x60000000))
#define TA0CCTL0 (HWREG16(0x60000002))
#define TA0CCTL1 (HWREG16(0x60000004))
#define TA0CCTL2 (HWREG16(0x60000006))
#define TA0CCTL3 (HWREG16(0x60000008))
#define TA0CCTL4 (HWREG16(0x6000000A))
#define TA0R (HWREG16(0x60000010))
/* More Register Macros Below */
MSP432_Version1.h
MSP432_Version2.h
#ifdef MSP432_VER1
#include “MSP432_Version1.h”
#else
#include “MSP432_Version2.h”
#endif
MSP432.h
$ make build PLATFORM=MSP432_VER1
Use Compile Time Switches to include correct Register Definition File

## Slide 9: Volatile Keyword [S7]
Volatile tells compiler NOT to optimize this code
  Volatile variable needs to be directly read and written when specified
Peripherals should be configured as soon as code executes, not moved to a later point in time
/ * 8, 16, & 32 Bit Register Access Macros */
#define HWREG8(x) (*((volatile uint8_t *)(x)))
#define HWREG16(x) (*((volatile uint16_t *)(x)))
#define HWREG32(x) (*((volatile uint32_t *)(x)))

## Slide 10: Structure Overlay [S8a]
Define a Structure to directly match peripheral region registers
typedef struct {
__IO uint16_t CTL;
__IO uint16_t CCTL[7];
__IO uint16_t R;
__IO uint16_t CCR[7];
__IO uint16_t EX0;
uint16_t RESERVED0[6];
__I uint16_t IV;
} Timer_A_Type;
#define __IO (volatile)
#define __I (volatile const)

## Slide 11: Structure Overlay [S8b]
Define a Structure to directly match peripheral region registers
/* Define the Base Address of Peripheral Regions */
#define PERIPH_BASE ((uint32_t) 0x40000000)
#define TIMER_A0_BASE (PERIPH_BASE + 0x00000000)
#define TIMER_A1_BASE (PERIPH_BASE + 0x00000400)
#define TIMER_A2_BASE (PERIPH_BASE + 0x00000800)
typedef struct {
__IO uint16_t CTL;
__IO uint16_t CCTL[7];
__IO uint16_t R;
__IO uint16_t CCR[7];
__IO uint16_t EX0;
uint16_t RESERVED0[6];
__I uint16_t IV;
} Timer_A_Type;
#define __IO (volatile)
#define __I (volatile const)

## Slide 12: Structure Overlay [S8c]
Define a Structure to directly match peripheral region registers
/* Define the Base Address of Peripheral Regions */
#define PERIPH_BASE ((uint32_t) 0x40000000)
#define TIMER_A0_BASE (PERIPH_BASE + 0x00000000)
#define TIMER_A1_BASE (PERIPH_BASE + 0x00000400)
#define TIMER_A2_BASE (PERIPH_BASE + 0x00000800)
/ * Multiple Timer Modules, different Addresses */
#define TIMER_A0 ((Timer_A_Type *) TIMER_A0_BASE)
#define TIMER_A1 ((Timer_A_Type *) TIMER_A1_BASE)
#define TIMER_A2 ((Timer_A_Type *) TIMER_A2_BASE)
typedef struct {
__IO uint16_t CTL;
__IO uint16_t CCTL[7];
__IO uint16_t R;
__IO uint16_t CCR[7];
__IO uint16_t EX0;
uint16_t RESERVED0[6];
__I uint16_t IV;
} Timer_A_Type;
TIMER_A0->CTL = 0x0202;
Example Use of Structure Overlay:
#define __IO (volatile)
#define __I (volatile const)

## Slide 13: Structure Overlay [S9]
Structure Overlays require exact replica of peripheral region
  Size registers to equivalent standard types
  Order Matters
  Leave space for reserved bytes
  Read-Only Registers = Const!
  All registers are volatile
typedef struct {
__IO uint16_t CTL;
__IO uint16_t CCTL[7];
__IO uint16_t R;
__IO uint16_t CCR[7];
__IO uint16_t EX0;
uint16_t RESERVED0[6];
__I uint16_t IV;
} Timer_A_Type;
#define __IO (volatile)
#define __I (volatile const)
Unused memory in the peripheral region

## Slide 14: Structure Overlay Example [S10]
Use Structure pointer and deference it to access the individual registers
typedef struct {
__IO uint16_t CTL;
__IO uint16_t CCTL[7];
__IO uint16_t R;
__IO uint16_t CCR[7];
__IO uint16_t EX0;
uint16_t RESERVED0[6];
__I uint16_t IV;
} Timer_A_Type;
TIMER_A0->CTL = 0x0202;
Example Use of Structure Overlay:
#define PERIPH_BASE ((uint32_t) 0x40000000)
#define TIMER_A0_BASE (PERIPH_BASE + 0x00000000)
#define TIMER_A0 ((Timer_A_Type *) TIMER_A0_BASE)
#define __IO (volatile)
#define __I (volatile const)

## Slide 15: Unused Slides
Ignore all slides below this

## Slide 16: Peripheral Memory [S2]
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
System Control Space (SCS)
Reserved
FPB
DWT
ITM (ETM)
Reserved
Reserved
MPU
Processor Debug Control
FPU
SCB
SysTick Timer
Misc system control registers
NVIC
Private Peripherals
General Peripherals

## Slide 17: Peripheral Registers in MSP432 [S1.3.6.c]
Peripheral Zone
Memory Map
Peripheral Region
0x5FFF_FFFF
0x4000_0000
Reserved
Peripheral Bit-Band Alias Region
Reserved
0x4400_0000
0x4200_0000
0x4010_0000
“4kB” peripheral region
(128kB for MSP432)

## Slide 18: Peripheral Registers in MSP432p401r [S1.3.6.c]
Peripheral Zone
Memory Map
Peripheral Region
0x5FFF_FFFF
0x4000_0000
Reserved
Peripheral Bit-Band Alias Region
Reserved
0x4400_0000
0x4200_0000
0x4010_0000
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Timer_A0
Port
Reserved
Peripheral Registers

## Slide 19: Peripheral Registers in MSP432p401r [S1.3.6.c]
Peripheral Region
0x5FFF_FFFF
0x4000_0000
Reserved
Peripheral Bit-Band Alias Region
Reserved
0x4400_0000
0x4200_0000
0x4010_0000
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Timer_A0
Port
Reserved
Timer_A0 Control
Timer_A0 CAPCOM Control 0
Timer_A0 Counter
Timer_A0 Interrupt Vector
Timer_A0 Expansion 0
Timer_A0 CAPCOM Control 1
Timer_A0 CAPCOM Control 2
Timer_A0 CAPCOM Control 3
Timer_A0 CAPCOM Control 4
Timer_A0 CAPCOM 0
Timer_A0 CAPCOM 1
Timer_A0 CAPCOM 2
Timer_A0 CAPCOM 3
Timer_A0 CAPCOM 4
Timer_A0 Registers
0x4000_0000
0x4000_0002
0x4000_0004
0x4000_0006
0x4000_0008
0x4000_000A
0x4000_0010
0x4000_0012
0x4000_0014
0x4000_0016
0x4000_0018
0x4000_001A
0x4000_002E
0x4000_0020
Peripheral Registers
Peripheral Zone
Memory Map