## Slide 1: IO Port Configuration Example
Embedded Software Essentials

## Slide 2: Peripherals [S1a]
Peripherals: External to CPU specialized support hardware
Similar process to configure peripherals
  Pointers
  Memory Reads/Writes
  Use of Bit Manipulation
Microcontroller
Flash
CPU
Peripherals
SRAM
Registers
Registers

## Slide 3: Peripherals [S1b]
Peripherals: External to CPU specialized support hardware
Similar process to configure peripherals
  Pointers
  Memory Reads/Writes
  Use of Bit Manipulation
GPIO – General Purpose Input/Output
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
LED

## Slide 4: Input Output Systems [S2a]
Microcontroller
Input/Output: method to get data in/out of microcontroller
  GIO
  IO
  GPIO (General Purpose IO)
GPIO Port
CPU
Peripherals
Registers
SPI
UART
ADC
Registers
Registers
Registers

## Slide 5: Input Output Systems [S2b]
Microcontroller
Input/Output: method to get data in/out of microcontroller
  GIO
  IO
  GPIO (General Purpose IO)
GPIO Port
CPU
Peripherals
Registers
SPI
UART
ADC
Registers
Registers
Registers
External Circuits
Multiple Pins

## Slide 6: Input Output Systems [S2c]
Microcontroller
Input/Output: method to get data in/out of microcontroller
  GIO
  IO
  GPIO (General Purpose IO)
Pin – physical connection to microcontroller
Port – combination of pins
GPIO Port
CPU
Peripherals
Registers
SPI
UART
ADC
Registers
Registers
Registers
External Circuits
Multiple Pins

## Slide 7: MSP432 Ports [S3a]
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 8: MSP432 Ports [S3b]
10 Ports
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 9: MSP432 Ports [S3c]
Port 1 – 8 Pins
GPIO / Primary / Secondary
Port 1 Pin 0 = P1.0
Primary Mode = SPI Chip Select
Port 1 Pin 7 = P1.7
Primary Mode = SPI Slave-Out-Master-In Data (UCB0SOMI)
Secondary Mode = I2C Clock (UCB0SCL)
10 Ports
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 10: MSP432 Ports [S4a]
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 11: MSP432 Ports [S4b]
P1.0 Red LED Circuit
LaunchPad Schematic: Microcontroller Connections
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 12: MSP432 Ports [S4a]
P1.0 Red LED Circuit
LED Schematic for P1.0
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 13: MSP432 Launchpad Schematic [S5a]
RED LED Schematic
Launchpad Schematic: MSP432 Pinout
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 14: MSP432 Launchpad Schematic [S5b]
Schematic Label for P1.0: P1.0_LED1
MSP432 Port 1
RED LED Schematic
Launchpad Schematic: MSP432 Pinout
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf
http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 15: MSP432 Launchpad Schematic [S5c]
MSP432 Pinout Port 1
MSP432 Pin Descriptions
Pin Modes
Pin Number
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf
http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 16: MSP432 Launchpad Schematic [S5d]
MSP432 Pinout Port 1
Pin Modes
Pin Number
MSP432 Pin Descriptions
Port P1Sel0.x /P1Sel1.x registers Select Mode for each Pin in Port
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf
http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 17: Configuring the LED [S6a]
To configure LED on P1.01
1Also Required to Set Pin to I/O Mode (P1SELx). This is set by default
Notes: http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 18: Configuring the LED [S6b]
To configure LED on P1.01
  Set direction to output (P1DIR)
1Also Required to Set Pin to I/O Mode (P1SELx). This is set by default
Notes: http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 19: Configuring the LED [S6c]
To configure LED on P1.01
  Set direction to output (P1DIR)
  Set P1.0 output to high (P1OUT)
1Also Required to Set Pin to I/O Mode (P1SELx). This is set by default
Notes: http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 20: Configuring the LED [S6d]
To configure LED on P1.01
  Set direction to output (P1DIR)
  Set P1.0 output to high (P1OUT)
To turn on LED, P1.0_LED1 voltage needs to be a Logical HIGH  VCC(3.3v)
1Also Required to Set Pin to I/O Mode (P1SELx). This is set by default
Notes: http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 21: Configuring the LED [S6e]
To configure LED on P1.01
  Set direction to output (P1DIR)
  Set P1.0 output to high (P1OUT)
To turn on LED, P1.0_LED1 voltage needs to be a Logical HIGH  VCC(3.3v)
1Also Required to Set Pin to I/O Mode (P1SELx). This is set by default
Notes: http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 22: Configuring IO Port [S7a]
Technical reference manual provides configuration steps
Digital IO has own section
  Important to read through this

## Slide 23: Configuring IO Port [S7b]
Two important registers
  IO Direction Register (P1DIR)
  IO Output Register (P1OUT)
Register section provides the software configuration steps using Bit Manipulation

## Slide 24: Configuring IO Port [S7c]
Two important registers
  IO Direction Register (PxDIR)
  IO Output Register (PxOUT)
PxOUT, PxDIR
  x = Port Number
Examples:
  P2OUT
  P1DIR

## Slide 25: P1DIR Register [S8a]
Port Direction Register sets pin to:
  0: an input
  1: an output

## Slide 26: P1DIR Register [S8b]
Port Direction Register sets pin to:
  0: an input
  1: an output
/* Configure P1.0 output */
P1->DIR |= BIT0;

## Slide 27: P1DIR Register [S8a]
Port Direction Register sets pin to:
  0: an input
  1: an output
/* Configure P1.0 output */
P1->DIR |= BIT0;
rw-0: Bit is Read/Write &
defaults to 0

## Slide 28: P1OUT Register [S9a]
Port Output Register sets output to:
  0: Output set to LOW (GND)
  1: Output set to HIGH (VCC)

## Slide 29: P1OUT Register [S9b]
Port Output Register sets output to:
  0: Output set to LOW (GND)
  1: Output set to HIGH (VCC)
/* Configure P1.0 output */
P1->DIR |= BIT0;
/* Set P1.0 HIGH */
P1->OUT |= BIT0;