## Slide 1: Debugging a Microcontroller Program: Part 1
Embedded Software Essentials
C2 M3 V7

## Slide 2: Testing Software [S1a]
Debugger: Software application that connects to embedded system’s target application
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Debugger Hardware
Host PC
Debug SW
DAP

## Slide 3: Testing Software [S1b]
Debugger: Software application that connects to embedded system’s target application
Debuggers allow users to
  Observe Behavior
  Control Behavior
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Debugger Hardware
Host PC
Debug SW
DAP
Debug Access Port (DAP)

## Slide 4: Testing Software [S1c]
Debugger: Software application that connects to embedded system’s target application
  E,g: GNU Debugger (gdb)
Debuggers allow users to
  Observe Behavior
  Control Behavior
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Debugger Hardware
Host PC
Debug SW
DAP
Debug Access Port (DAP)
gdb
*Not always required

## Slide 5: Debuggers [S2a]
Main Tasks:
  Connect to development board
  Program an application
  Debug an application
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Debugger Hardware
Host PC
Debug SW
DAP
gdb
Notes: Addison, C. (2015, December 11). Code Composer Studio v6 [Digital image]. Retrieved November 08, 2016, from https://e2e.ti.com/blogs_/b/toolsinsider/archive/2015/12/11/helpful-tips-executing-code-from-ram

## Slide 6: Debuggers [S2a]
Main Tasks:
  Connect to development board
  Program an application
  Debug an application
Requires software application running on a host machine
Host PC
Debug SW
XDS-110ET
On Board Programmer / Debugger
DAP is internal to target Microcontroller
Notes: http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 7: Debuggers [S2c]
Main Tasks:
  Connect to development board
  Program an application
  Debug an application
Requires software application running on a host machine
  Code Composer Studio (CCS)
    Texas Instruments IDE with Debugger
XDS-110ET
On Board Programmer / Debugger
DAP is internal to target Microcontroller
Notes: Addison, C. (2015, December 11). Code Composer Studio v6 [Digital image]. Retrieved November 08, 2016, from https://e2e.ti.com/blogs_/b/toolsinsider/archive/2015/12/11/helpful-tips-executing-code-from-ram
http://www.ti.com/lit/ug/slau597c/slau597c.pdf

## Slide 8: Debug Symbols [S3]
Microcontroller
Must enable debug symbols at compilation
  -g flag
Provides mechanism for debugger to interpret executing code and map to original source code
Executing Application
(Machine Code)
Debug Application
Source Code
Symbol Table
$ arm-none-eabi-gcc –g main.c –o main.o
DAP
Memory (SRAM/Flash)
Commands and Data Sent between application and Microcontroller)

## Slide 9: Debug Access Port [S4a]
Built in debug port called Debug Access Port (DAP)
Supports multiple debugging interfaces
  Joint Test Action Group (JTAG)
  Serial Wire Debug (SWD)
Notes: http://www.ti.com/lit/ug/slau356f/slau356f.pdf

## Slide 10: Debug Access Port [S4a]
Built in debug port called Debug Access Port (DAP)
Supports multiple debugging interfaces
  Joint Test Action Group (JTAG)
  Serial Wire Debug (SWD)
Notes: http://www.ti.com/lit/ug/slau356f/slau356f.pdf

## Slide 11: Breakpoints [S5a]
Mechanism to stop or pause the current execution of a program
  Program must be un-paused or restarted a breakpoint occurs
Limited number of breakpoints allowed
blink.c

## Slide 12: Breakpoints [S5b]
Mechanism to stop or pause the current execution of a program
  Program must be un-paused or restarted a breakpoint occurs
Limited number of breakpoints allowed
blink.c
Breakpoint Indicator
Pause
Play
Step Into
Step Over
Step Out

## Slide 13: Watch Points [S6a]
Mechanism to stop or pause the current execution of a program when a variable or expression changes
Can happen at any point in the program
uint32_t i = 0;
for (i = 0; i < 16; i++)
{
/* Other Code Here*/
}
Example:
Set watch point on variable i. Anytime i changes, break. This should occur 16 times in this code excerpt

## Slide 14: Breakpoints & Watchpoints [S7a]
Microcontroller can miss data or external events if processor is paused
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
DAP
Debugger Hardware
Host PC
Debug SW
Serial device
(UART)
UART
Registers
TX
RX
Serial device is transmitting sequence of packets

## Slide 15: Variable Scope [S8a]
Variables view allows you to see value while in current scope
Must be paused to read value
Can inject any value during a pause for testing
Before Initialization
After Initialization
Before Entry to Main

## Slide 16: Expressions [S9a]
Expressions view allows you to see any global variable, register or general expression
Can write c-expressions in here and they are evaluated at runtime
Must be paused to read values
Breakpoint after array1 initialized

## Slide 17: Registers [S10a]
Register view allows you to view
  Core CPU Registers
    General Purpose
    Special Purpose
  Peripheral Registers
Must be paused to read values
Can inject any value into register bit fields during a pause for testing

## Slide 18: Memory Browser [S11a]
Memory Browser allows you to view and alter memory directly at different accessible addresses
Can format memory view many ways
Must be paused to read values
array1 & array2 addresses

## Slide 19: Stack Trace [S12a]
Allows you to determine the function call hierarchy by looking at the stack
  Stack provides history of call frames
Must be paused to read current call stack
Very helpful for multi-threaded programs
Main calls blink_led_forever()
Main is called by _c_int00()