## Slide 1: Memory Access and Manipulation
Embedded Software Essentials

## Slide 2: Microcontroller Varieties [S1a]
Manufacturers have multiple chips in a family with varying features
  Flash
  SRAM
  Peripherals
Microcontroller Architecture Family

## Slide 3: Microcontroller Varieties [S1b]
Manufacturers have multiple chips in a family with varying features
  Flash
  SRAM
  Peripherals
Flash
128KB
CPU
ARM Cortex-M3
Peripherals
4x Timer/PWM
16 Ch. ADC
3 USCI (SPI/I2C/USART)
SRAM
16KB
Flash
256KB
CPU
ARM Cortex-M4
Peripherals
8x Timer/PWM
24 Ch. ADC
6x USCI (SPI/I2C/USART)
1x USB
1x DAC
4 Ch. DMA
SRAM
32KB
Microcontroller A
Microcontroller B
Microcontroller Architecture Family

## Slide 4: Microcontroller Varieties [S1c]
Manufacturers have multiple chips in a family with varying features
  Flash
  SRAM
  Peripherals
Important to track platform differences in your software
Flash
128KB
CPU
ARM Cortex-M3
Peripherals
4x Timer/PWM
16 Ch. ADC
3 USCI (SPI/I2C/USART)
SRAM
16KB
Flash
256KB
CPU
ARM Cortex-M4
Peripherals
8x Timer/PWM
24 Ch. ADC
6x USCI (SPI/I2C/USART)
1x USB
1x DAC
4 Ch. DMA
SRAM
32KB
Microcontroller A
Microcontroller B
Microcontroller Architecture Family

## Slide 5: Microcontroller Varieties [S1d]
Manufacturers have multiple chips in a family with varying features
  Flash
  SRAM
  Peripherals
Important to track platform differences in your software
Flash
128KB
CPU
ARM Cortex-M3
Peripherals
4x Timer/PWM
16 Ch. ADC
3 USCI (SPI/I2C/USART)
SRAM
16KB
Register Definition File
Linker File
Compiler Toolchain
Flash
256KB
CPU
ARM Cortex-M4
Peripherals
8x Timer/PWM
24 Ch. ADC
6x USCI (SPI/I2C/USART)
1x USB
1x DAC
4 Ch. DMA
SRAM
32KB
Microcontroller A
Microcontroller B
Microcontroller Architecture Family

## Slide 6: Embedded System Memories [S2a]
Memories of an Embedded System
  Code Memory (Flash)
  Data Memory (SRAM)
  Register Memory
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers

## Slide 7: Embedded System Memories [S2b]
Memories of an Embedded System
  Code Memory (Flash)
  Data Memory (SRAM)
  Register Memory
All processing occurs in CPU
  Data is loaded into register and then stored back to memory
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Registers
Registers
Registers
Pointers used to interact with memory

## Slide 8: Embedded System Memories [S3a]
CPU registers constantly change
  Data is loaded in from memory
  Data is stored back to memory
CPU
Bus Interface
SRAM
Store from
R10
Load into
R4
Data manipulation needed at bit level

## Slide 9: Embedded System Memories [S3b]
CPU registers constantly change
  Data is loaded in from memory
  Data is stored back to memory
Bit Manipulation used to configure microcontrollers
CPU
Bus Interface
SRAM
Store from
R10
Load into
R4
Data manipulation needed at bit level

## Slide 10: Embedded System Memories [S3c]
CPU registers constantly change
  Data is loaded in from memory
  Data is stored back to memory
Bit Manipulation used to configure microcontrollers
CPU
Bus Interface
SRAM
Store from
R10
Load into
R4
Data manipulation needed at bit level
Use of Bitwise and Arithmetic Operators!

## Slide 11: Peripherals [S4a]
Peripherals: External to CPU specialized support hardware
Microcontroller
Cortex-M
SRAM Memory
Flash Memory
Flash
Controller
AHB Flash I-code Bus
AHB Flash
D-code Bus
High-Speed Peripheral
AHB System
Bus
Bridge
Peripherals
Peripherals
Peripherals
APB
Peripheral
Bus
PPB (Internal)
Internal Private Peripherals
PPB (External)
Debugger

## Slide 12: Peripherals [S4b]
Peripherals: External to CPU specialized support hardware
Microcontroller
Cortex-M
SRAM Memory
Flash Memory
Flash
Controller
AHB Flash I-code Bus
AHB Flash
D-code Bus
High-Speed Peripheral
AHB System
Bus
Bridge
Peripherals
Peripherals
Peripherals
APB
Peripheral
Bus
PPB (Internal)
Internal Private Peripherals
PPB (External)
Debugger
Many Different Types:
High / Low Speed
Internal / External to CPU

## Slide 13: Peripherals [S4c]
Peripherals: External to CPU specialized support hardware
Technical Reference Manual provides configuration guide
  Functional Description
  Register Description
  Addresses
  Order of Operations
Microcontroller
Cortex-M
SRAM Memory
Flash Memory
Flash
Controller
AHB Flash I-code Bus
AHB Flash
D-code Bus
High-Speed Peripheral
AHB System
Bus
Bridge
Peripherals
Peripherals
Peripherals
APB
Peripheral
Bus
PPB (Internal)
Internal Private Peripherals
PPB (External)
Debugger
Many Different Types:
High / Low Speed
Internal / External to CPU

## Slide 14: Timer A0 Peripheral [S5a]
Peripherals have multiple registers
  Status
  Control
  Data
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
Peripheral Devices
Peripheral Zone
Memory Map
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 15: Timer A0 Peripheral [S5b]
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
Timer_A0 Control
Timer_A0 CAPCOM Control 0
Timer_A0 Counter
Timer_A0 Interrupt Vector
Timer_A0 Expansion 0
Timer_A0 CAPCOM Control 1
Timer_A0 CAPCOM Control 2
Timer_A0 CAPCOM Control 3
Timer_A0 CAPCOM Control 4
Timer_A0 CAPCOM 0
Timer_A0 CAPCOM 1
Timer_A0 CAPCOM 2
Timer_A0 CAPCOM 3
Timer_A0 CAPCOM 4
Timer_A0 Registers
0x40000000
0x40000002
0x40000004
0x40000006
0x40000008
0x4000000A
0x40000010
0x40000012
0x40000014
0x40000016
0x40000018
0x4000001A
0x4000002E
0x40000020
Peripheral Devices
Peripheral Zone
Memory Map
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Peripherals have multiple registers
  Status
  Control
  Data
Addresses to use with pointers
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 16: Timer A0 Peripheral [S5c]
Timer_A0 Control
Timer_A0 CAPCOM Control 0
Timer_A0 Counter
Timer_A0 Interrupt Vector
Timer_A0 Expansion 0
Timer_A0 CAPCOM Control 1
Timer_A0 CAPCOM Control 2
Timer_A0 CAPCOM Control 3
Timer_A0 CAPCOM Control 4
Timer_A0 CAPCOM 0
Timer_A0 CAPCOM 1
Timer_A0 CAPCOM 2
Timer_A0 CAPCOM 3
Timer_A0 CAPCOM 4
Timer_A0 Registers
0x40000000
0x40000002
0x40000004
0x40000006
0x40000008
0x4000000A
0x40000010
0x40000012
0x40000014
0x40000016
0x40000018
0x4000001A
0x4000002E
0x40000020
Peripherals have multiple registers
  Status
  Control
  Data
/* Timer Peripheral Device Structure Overlay */
typedef struct {
__IO uint16_t CTL;
__IO uint16_t CCTL[7];
__IO uint16_t R;
__IO uint16_t CCR[7];
__IO uint16_t EX0;
uint16_t RESERVED0[6];
__I uint16_t IV;
} Timer_A_Type;
/* Define the Base Address of Peripheral Regions */
#define PERIPH_BASE ((uint32_t) 0x40000000)
#define TIMER_A0_BASE (PERIPH_BASE+0x00000000)
/ * Multiple Timer Modules, Different Addresses */
#define TIMER_A0 ((Timer_A_Type *) TIMER_A0_BASE)
…
Register Definition File (msp.h)
Notes: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0553a/CHDBIBGJ.html

## Slide 17: Code Improvements [S6a]
General improvements can include
  Runtime Optimizations
  Architectural Improvements
  Dynamic Function Calling
int main(){
int a_STACK = 10;
int data;
data = foo(a_STACK);
return 0;
}
int foo(int D_STACK_IN){
int b_STACK;
char * ptr_STACK;
/* More Code Here */
return b_STACK;
}

## Slide 18: Code Improvements [S6b]
General improvements can include
  Runtime Optimizations
  Architectural Improvements
  Dynamic Function Calling
int main(){
int a_STACK = 10;
int data;
data = foo(a_STACK);
return 0;
}
int foo(int D_STACK_IN){
int b_STACK;
char * ptr_STACK;
/* More Code Here */
return b_STACK;
}
Example: Reducing function call overhead due branch and register/state saving

## Slide 19: Hardware Abstraction [S7]
Abstract hardware layers from higher level software
  Example: Input Output Library
Higher level software should be independent of low level firmware
GPIO Hardware
IO.c
IO_Read()
IO_Write()
IO_Configrue()
Peripheral & Hardware Layer
Bare-Metal
Firmware
High Level Software – blink_LEDs.c
LED
LED
LED
LED
External Hardware
Application