## Slide 1: Bit Manipulation
Embedded Software Essentials

## Slide 2: Bit Manipulation [S1a]
Bit Manipulation used to configure microcontrollers
Generalized ARM CPU
Result
Arithmetic Logic
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction
PSR
Mask Registers
Control
Special Function
Registers

## Slide 3: Bit Manipulation [S1b]
Bit Manipulation used to configure microcontrollers
All arithmetic operations can be done with bitwise operations
Generalized ARM CPU
Result
Arithmetic Logic
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction
PSR
Mask Registers
Control
Special Function
Registers

## Slide 4: Bit Manipulation [S1c]
Bit Manipulation used to configure microcontrollers
All arithmetic operations can be done with bitwise operations
Generalized ARM CPU
Result
Arithmetic Logic
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction
PSR
Mask Registers
Control
Special Function
Registers
Made of Logic Gates

## Slide 5: Bit Manipulation [S1d]
Bit Manipulation used to configure microcontrollers
All arithmetic operations can be done with bitwise operations
Bitwise operators are needed to configure peripherals
Generalized ARM CPU
Result
Arithmetic Logic
Unit (ALU)
General Purpose Registers
Stack pointer
Program Counter
Instruction
PSR
Mask Registers
Control
Special Function
Registers
Made of Logic Gates

## Slide 6: Bitwise Operators [S2a]
Peripheral registers require some contents (bit-fields) to be preserved
Use bit manipulation to change certain bits of a register (not all contents)
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers

## Slide 7: Bitwise Operators [S2b]
Peripheral registers require some contents (bit-fields) to be preserved
Use bit manipulation to change certain bits of a register (not all contents)
C-programming provides bitwise operators
  << >> & | ^ ~
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers

## Slide 8: Bitwise Operators [S2c]
Peripheral registers require some contents (bit-fields) to be preserved
Use bit manipulation to change certain bits of a register (not all contents)
C-programming provides bitwise operators
  << >> & | ^ ~
? | ? | ? | ? | ? | ? | ? | ?
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
? | ? | ? | 1 | ? | ? | ? | ?
foo
foo
foo = foo | 0x10;
0x10
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers

## Slide 9: Bitwise Operators [S3a]
C-programming provides bitwise operators
  << >> & | ^ ~
*ptr |= 0x10;
Set 4th bit:
*ptr ^= 0x10;
Toggle 4th bit:
uint8_t * ptr = (uint8_t *)0x1000;
*ptr &= ~(0x10);
Clear 4th bit:

## Slide 10: Bitwise Operators [S3b]
C-programming provides bitwise operators
  << >> & | ^ ~
*ptr |= 0x10;
Set 4th bit:
*ptr ^= 0x10;
Toggle 4th bit:
uint8_t * ptr = (uint8_t *)0x1000;
*ptr &= ~(0x10);
Clear 4th bit:
All bits preserved except bit 4 using logical assignment combination

## Slide 11: Bitwise Operators [S3c]
C-programming provides bitwise operators
  << >> & | ^ ~
*ptr |= 0x10;
Set 4th bit:
*ptr ^= 0x10;
Toggle 4th bit:
uint8_t * ptr = (uint8_t *)0x1000;
*ptr &= ~(0x10);
Clear 4th bit:
All bits preserved except bit 4 using logical assignment combination
Combine logic with assignment, performs a read, modify, write

## Slide 12: Bitwise Example: OR [S4a]
uint8_t foo = 0x84;
foo = foo | 0x30;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Set Bits 4 & 5:

## Slide 13: Bitwise Example: OR [S4b]
uint8_t foo = 0x84;
foo = foo | 0x30;
This performs a READ to load foo into CPU registers
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Set Bits 4 & 5:

## Slide 14: Bitwise Example: OR [S4c]
uint8_t foo = 0x84;
foo = foo | 0x30;
This performs a READ to load foo into CPU registers
Performs a
WRITE to
update memory
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Set Bits 4 & 5:

## Slide 15: Bitwise Example: OR [S4d]
uint8_t foo = 0x84;
foo |= 0x30;
Still performs a Read, Modify, Write
Provides a cleaner shorthand for same expression
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
foo |= (0x03 << 4);
Alternatively:
Set Bits 4 & 5:

## Slide 16: Bitwise Example: & [S5a]
uint8_t foo = 0xFF;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Clear Bits 6 & 7:

## Slide 17: Bitwise Example: & [S5b]
uint8_t foo = 0xFF;
foo = foo & 0x3F;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Clear Bits 6 & 7:
Results in clearing bits 6 & 7

## Slide 18: Bitwise Example: & [S5c]
uint8_t foo = 0xFF;
foo &= 0x3F;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Clear Bits 6 & 7:

## Slide 19: Bitwise Example: & [S5d]
uint8_t foo = 0xFF;
foo &= ~(0xC0);
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Clear Bits 6 & 7:
~(0xC0)  0x3F
Specifying bits you wish to clear is more readable

## Slide 20: Bitwise Example: TOGGLE [S6a]
uint8_t foo = 0x0C;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Toggle Bits 1, 2, & 3:

## Slide 21: Bitwise Example: TOGGLE [S6b]
uint8_t foo = 0x0C;
foo = foo ^ 0x0E;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Toggle Bits 1, 2, & 3:
Results in 0x02

## Slide 22: Bitwise Example: TOGGLE [S6c]
uint8_t foo = 0x0C;
foo = foo ^ 0x0E;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Toggle Bits 1, 2, & 3:
Results in 0x02
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
foo
foo
0x0E

## Slide 23: Bitwise Example: TOGGLE [S6d]
uint8_t foo = 0x0C;
foo ^= 0x0E;
Microcontroller
Code Memory
CPU
Peripherals
Data Memory
Registers
Registers
Toggle Bits 1, 2, & 3:
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
foo
foo
0x0E

## Slide 24: Bit Masks [S7a]
Bit Masks are constant expressions used to set, clear, or toggle a specific set of bits
foo |= 0x30 ;
foo &= ~( 0xC0 );
foo ^= 0x0E ;

## Slide 25: Bit Masks [S7b]
Bit Masks are constant expressions used to set, clear, or toggle a specific set of bits
foo |= 0x30 ;
foo &= ~( 0xC0 );
foo ^= 0x0E ;
Use Preprocessors to make code more readable
#define MASK1 (0x30)
#define MASK2 (0xC0)
#define MASK3 (0x0E)

## Slide 26: Bit Masks [S7c]
Bit Masks are constant expressions used to set, clear, or toggle a specific set of bits
foo |= 0x30 ;
foo &= ~( 0xC0 );
foo ^= 0x0E ;
Use Preprocessors to make code more readable
#define MASK1 (0x30)
#define MASK2 (0xC0)
#define MASK3 (0x0E)
foo |= MASK1 ;
foo &= MASK2 ;
foo ^= MASK3 ;

## Slide 27: Bit Masks [S8a]
Bit Masks are constant expressions used to set, clear, or toggle a specific set of bits
foo |= 0x30 ;
foo &= ~( 0xC0 );
foo ^= 0x0E ;
#define BIT0 (uint16_t)(0x0001)
#define BIT1 (uint16_t)(0x0002)
#define BIT2 (uint16_t)(0x0004)
#define BIT3 (uint16_t)(0x0008)
#define BIT4 (uint16_t)(0x0010)
#define BIT5 (uint16_t)(0x0020)
#define BIT6 (uint16_t)(0x0040)
#define BIT7 (uint16_t)(0x0080)
#define BIT8 (uint16_t)(0x0100)
#define BIT9 (uint16_t)(0x0200)
#define BITA (uint16_t)(0x0400)
#define BITB (uint16_t)(0x0800)
#define BITC (uint16_t)(0x1000)
#define BITD (uint16_t)(0x2000)
#define BITE (uint16_t)(0x4000)
#define BITF (uint16_t)(0x8000)
Example Bit Defines from Texas Instruments msp.h Header Files
msp.h

## Slide 28: Bit Masks [S7d]
Bit Masks are constant expressions used to set, clear, or toggle a specific set of bits
foo |= (BIT4 | BIT5);
foo &= ~( BIT7 | BIT6 );
foo ^= (BIT3 | BIT2 | BIT1);
#define BIT0 (uint16_t)(0x0001)
#define BIT1 (uint16_t)(0x0002)
#define BIT2 (uint16_t)(0x0004)
#define BIT3 (uint16_t)(0x0008)
#define BIT4 (uint16_t)(0x0010)
#define BIT5 (uint16_t)(0x0020)
#define BIT6 (uint16_t)(0x0040)
#define BIT7 (uint16_t)(0x0080)
#define BIT8 (uint16_t)(0x0100)
#define BIT9 (uint16_t)(0x0200)
#define BITA (uint16_t)(0x0400)
#define BITB (uint16_t)(0x0800)
#define BITC (uint16_t)(0x1000)
#define BITD (uint16_t)(0x2000)
#define BITE (uint16_t)(0x4000)
#define BITF (uint16_t)(0x8000)
Example Bit Defines from Texas Instruments msp.h Header Files
msp.h

## Slide 29: Peripheral Configuration [S9a]
Often need to combine set and clear to create desired effect without destroying other bit values

## Slide 30: Peripheral Configuration [S9b]
Often need to combine set and clear to create desired effect without destroying other bit values
Example
  Set Bits: 4 & 5
  Clear Bits: 6 & 7
  Preserve Other Bit Values
Set with | (OR)
Clear with & / ~ (AND/Complement)
Combine logic and assignment

## Slide 31: Peripheral Configuration [S10a]
Often need to combine set and clear to create desired effect without destroying other bit values
Example
  Set Bits: 4 & 5
  Clear Bits: 6 & 7
  Preserve Other Bit Values
? | ? | ? | ? | ? | ? | ? | ?
C | C | S | S |  |  |  | 
0 | 0 | 1 | 1 | ? | ? | ? | ?
*ptr
*ptr (after)

## Slide 32: Peripheral Configuration [S10b]
Often need to combine set and clear to create desired effect without destroying other bit values
Example
  Set Bits: 4 & 5
  Clear Bits: 6 & 7
  Preserve Other Bit Values
uint8_t * ptr = (uint8_t *)0x40004C02;
*ptr &= ~(BIT6 | BIT7) ;
*ptr |= (BIT4 | BIT5);
? | ? | ? | ? | ? | ? | ? | ?
C | C | S | S |  |  |  | 
0 | 0 | 1 | 1 | ? | ? | ? | ?
*ptr
*ptr (after)

## Slide 33: Bit Banded Memory [S11a]
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
General Peripherals
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved

## Slide 34: Bit Banded Memory [S11b]
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
General Peripherals
SRAM Region
Reserved
SRAM Bit-Band Alias Region
Reserved
First 1MB of SRAM and Peripheral have a bit-band alias

## Slide 35: Bit Band Alias [S12a]
Each bit in the Peripheral & SRAM region is bit addressable
  Bits are word aligned
0x20000001
0x20000002
0x20000000
Address
0x20000003
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Bits
Alias: 0x2200003C
Alias: 0x22000010
Alias: 0x22000000

## Slide 36: Bit Band Alias [S12b]
Each bit in the Peripheral & SRAM region is bit addressable
  Bits are word aligned
Alias region is offset 0x02000000
  Peripheral Bit Band: 0x42000000
  SRAM Bit Band: 0x22000000
Allows single bit to be read or written to
0x20000001
0x20000002
0x20000000
Address
0x20000003
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Bits
Alias: 0x2200003C
Alias: 0x22000010
Alias: 0x22000000

## Slide 37: Bit Band Effects [S13a]
Negatives
  Reduces the overall available memory for other hardware
0x20000001
0x20000002
0x20000000
Address
0x20000003
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Bits
Alias: 0x2200003C
Alias: 0x22000010
Alias: 0x22000000

## Slide 38: Bit Band Effects [S13b]
Negatives
  Reduces the overall available memory for other hardware
Positives
  Reduces number of instructions needed for read, modify, write
0x20000001
0x20000002
0x20000000
Address
0x20000003
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Bits
Alias: 0x2200003C
Alias: 0x22000010
Alias: 0x22000000

## Slide 39: Bit Band Effects [S13c]
Negatives
  Reduces the overall available memory for other hardware
Positives
  Reduces number of instructions needed for read, modify, write
    Operation is atomic
0x20000001
0x20000002
0x20000000
Address
0x20000003
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Bits
Alias: 0x2200003C
Alias: 0x22000010
Alias: 0x22000000
Only one instruction is needed and it cannot be interrupted