## Slide 1: Creating Software Interfaces for Hardware
Embedded Software Essentials

## Slide 2: Platform Independence [S1a]
Microcontrollers have a variety of
  Peripherals
  Registers
  Memories
Software Architecture: structured organization of a software project
Design software to be independent of architecture and platform1
May have 1000+ peripheral registers.
1Impossible to remove all hardware dependencies
Notes: http://www.ti.com/lit/ds/symlink/msp432p401m.pdf

## Slide 3: Platform Independence [S1b]
MSP432 Platform
Executable Program
Bare Metal Firmware
Abstraction Layer
Application
Microcontrollers have a variety of
  Peripherals
  Registers
  Memories
Software Architecture: structured organization of a software project
Design software to be independent of architecture and platform1
Executable stored in Flash

## Slide 4: Abstraction Layers [S2a]
MSP432
SPI Peripheral
GPIO Hardware
spi.c
platform_msp432.c
port.c
Application
msp432p401r.h
Firmware layer needs to be efficient and bug-free
Make higher level software independent of low level firmware
  Example: application software
Hardware
Layer
Firmware
Application
Specific
$ make all PLATFORM=MSP432

## Slide 5: Abstraction Layers [S2b]
Hardware
Layers
KL25z
SPI Peripheral
GPIO Hardware
spi.c
platform_kl25z.c
port.c
Application
MKL25Z.h
$ make all PLATFORM=KL25Z
Register Definition Files
MSP432
SPI Peripheral
GPIO Hardware
spi.c
platform_msp432.c
port.c
Application
msp432p401r.h
Same Application, Different Firmware and Platform code

## Slide 6: Abstraction Layers [S2c]
Hardware
Layers
KL25z
SPI Peripheral
GPIO Hardware
spi.c
platform_kl25z.c
port.c
Application
MKL25Z.h
$ make all PLATFORM=KL25Z
Same Application, Different Firmware and Platform code
Register Definition Files
Interface methods for hardware
  Register Definition Files
  Macro Functions
  Specialized C-Functions

## Slide 7: Embedded Hardware Interface [S4a]
Interface methods for hardware
  Register Definition Files
  Macro Functions
  Specialized C-Functions
MSP432
SPI Peripheral
GPIO Hardware
spi.c
platform_msp432.c
port.c
Application
msp432p401r.h
ARM Core
CMSIS
Notes: https://www.arm.com/products/processors/cortex-m/cortex-microcontroller-software-interface-standard.php

## Slide 8: Embedded Hardware Interface [S4b]
Interface methods for hardware
  Register Definition Files
  Macro Functions
  Specialized C-Functions
Create Hardware Abstraction Layer (HAL) to simplify application level programming
  Acts like an API (Application Programming Interface)
MSP432
SPI Peripheral
GPIO Hardware
spi.c
platform_msp432.c
port.c
Application
msp432p401r.h
ARM Core
CMSIS
Notes: https://www.arm.com/products/processors/cortex-m/cortex-microcontroller-software-interface-standard.php

## Slide 9: Embedded Hardware Interface [S4c]
Create Hardware Abstraction Layer (HAL) to simplify application level programming
MSP432
SPI Peripheral
GPIO Hardware
spi.c
platform_msp432.c
port.c
Application
msp432p401r.h
ARM Core
CMSIS
ARM Core Microcontroller Software Interface Standard (CMSIS) Diagram
Notes: https://www.arm.com/products/processors/cortex-m/cortex-microcontroller-software-interface-standard.php

## Slide 10: Register Definition Files [S5a]
Platform File that provides interface to peripheral memory by specifying
  Address List for Peripherals
  Access Methods
  Defines for Bit Fields and Bit Masks
Timer_A0-A3
eUSCI_A0-A3
eUSCI_B0-B3
REF_A
COMP_E0-E1
AES256
CRC32
RTC_C
WDT_A
Timer32
ADC14
Port
Reserved
Reserved
MPU
Processor Debug Control
FPU
SCB
SysTick Timer
Misc system control registers
NVIC
General
Peripherals
Private
Peripherals
Could Contain 1000’s of Registers!

## Slide 11: Register Definition Files [S5b]
Platform File that provides interface to peripheral memory by specifying
  Address List for Peripherals
  Access Methods
  Defines for Bit Fields and Bit Masks
Peripheral Access Methods used to read/write data
  Preprocessor Macros
  Direct Dereferencing of Memory
  Structure Overlays
MSP432
SPI Peripheral
GPIO Hardware
Application
msp432p401r.h
ARM Core
CMSIS

## Slide 12: Register Definition Files [S5c]
Platform File that provides interface to peripheral memory by specifying
  Address List for Peripherals
  Access Methods
  Defines for Bit Fields and Bit Masks
Peripheral Access Methods used to read/write data
  Preprocessor Macros
  Direct Dereferencing of Memory
  Structure Overlays
MSP432
SPI Peripheral
GPIO Hardware
Application
msp432p401r.h
ARM Core
CMSIS
Platform and architecture software interface

## Slide 13: Register Definition Files [S5d]
Platform File that provides interface to peripheral memory by specifying
  Address List for Peripherals
  Access Methods
  Defines for Bit Fields and Bit Masks
Peripheral Access Methods used to read/write data
  Preprocessor Macros
  Direct Dereferencing of Memory
  Structure Overlays
Direct Application dependency on platform and core architecture
MSP432
SPI Peripheral
GPIO Hardware
Application
msp432p401r.h
ARM Core
CMSIS

## Slide 14: Embedded Hardware Interface [S6a]
Interface methods for hardware
  Register Definition Files
  Macro Functions
  Specialized C-Functions

## Slide 15: Embedded Hardware Interface [S6b]
Interface methods for hardware
  Register Definition Files
  Macro Functions
  Specialized C-Functions
Regularly used in firmware abstraction

## Slide 16: Embedded Hardware Interface [S6c]
Interface methods for hardware
  Register Definition Files
  Macro Functions
  Specialized C-Functions
Regularly used in firmware abstraction
/* Macro Function to Read Memory */
#define HWREG16(x) (*((volatile uint16_t *)(x)))
Platform Dependency

## Slide 17: Embedded Hardware Interface [S6d]
Interface methods for hardware
  Register Definition Files
  Macro Functions
  Specialized C-Functions
Regularly used in firmware abstraction
/* Macro Function to Read Memory */
#define HWREG16(x) (*((volatile uint16_t *)(x)))
/* Specialized CMSIS Function to Enable Interrupts */
__attribute__( ( always_inline ) ) __STATIC_INLINE void __enable_irq(void)
{
__ASM volatile ("cpsie i" : : : "memory");
}
Platform Dependency
Architecture Dependency

## Slide 18: Macro Functions [S7a]
Direct Substitution in code
#define TA0CTL_ADDR (0x40000000)
/ * 16 Bit Register Access Macros */
#define HWREG16(x) (*((volatile uint16_t *)(x)))

## Slide 19: Macro Functions [S7b]
Direct Substitution in code
#define TA0CTL_ADDR (0x40000000)
/ * 16 Bit Register Access Macros */
#define HWREG16(x) (*((volatile uint16_t *)(x)))
Not an actual function call, no calling convention overhead!

## Slide 20: Macro Functions [S7c]
Direct Substitution in code
Example use of access method:
#define TA0CTL_ADDR (0x40000000)
/ * 16 Bit Register Access Macros */
#define HWREG16(x) (*((volatile uint16_t *)(x)))
HWREG16(TA0CTL_ADDR) = 0x0202;
(*((volatile uint16_t *)(0x40000000))) = 0x0202;

## Slide 21: Macro Functions [S7d]
/ * 8, 16, & 32 Bit Register Access Macros */
#define HWREG8(x) (*((volatile uint8_t *)(x)))
#define HWREG16(x) (*((volatile uint16_t *)(x)))
#define HWREG32(x) (*((volatile uint32_t *)(x)))
#define TA0CTL (HWREG16(0x40000000))
TA0CTL = 0x0202;
volatile uint16_t * ta0_ctrl = (uint16_t*)0x40000000;
*ta0_ctrl = 0x0202;
Example Use of Access Macro:
Same

## Slide 22: Macro Functions [S7e]
/ * 8, 16, & 32 Bit Register Access Macros */
#define HWREG8(x) (*((volatile uint8_t *)(x)))
#define HWREG16(x) (*((volatile uint16_t *)(x)))
#define HWREG32(x) (*((volatile uint32_t *)(x)))
#define TA0CTL (HWREG16(0x40000000))
Pass in any address to access a register
TA0CTL = 0x0202;
volatile uint16_t * ta0_ctrl = (uint16_t*)0x40000000;
*ta0_ctrl = 0x0202;
Example Use of Access Macro:
Same

## Slide 23: Port Macros [S8a]
/ * 8, 16, & 32 Bit Register Access Macros */
#define HWREG8(x) (*((volatile uint8_t *)(x)))
#define HWREG16(x) (*((volatile uint16_t *)(x)))
#define HWREG32(x) (*((volatile uint32_t *)(x)))
Generic memory access macro for different sized registers
  8, 16, 32 Bit Registers
/ * Port 1 Register Access Macros */
#define P1IN (HWREG8(0x40004C00))
#define P1OUT (HWREG8(0x40004C02))
#define P1DIR (HWREG8(0x40004C04))
#define P1SEL0 (HWREG8(0x40004C0A))
#define P1SEL1 (HWREG8(0x40004C0C))
#define P1IES (HWREG8(0x40004C18))
#define P1IE (HWREG8(0x40004C1A))

## Slide 24: Port Macros [S8b]
/ * 8, 16, & 32 Bit Register Access Macros */
#define HWREG8(x) (*((volatile uint8_t *)(x)))
#define HWREG16(x) (*((volatile uint16_t *)(x)))
#define HWREG32(x) (*((volatile uint32_t *)(x)))
Generic memory access macro for different sized registers
  8, 16, 32 Bit Registers
Port registers use the generalized access macros
/ * Set P1.0 to Output Direction */
P1DIR |= 0x01;
/ * Port 1 Register Access Macros */
#define P1IN (HWREG8(0x40004C00))
#define P1OUT (HWREG8(0x40004C02))
#define P1DIR (HWREG8(0x40004C04))
#define P1SEL0 (HWREG8(0x40004C0A))
#define P1SEL1 (HWREG8(0x40004C0C))
#define P1IES (HWREG8(0x40004C18))
#define P1IE (HWREG8(0x40004C1A))

## Slide 25: Port Macros [S8c]
#define SET_PORT_PIN_DIR (port, pin) ( (port)->DIR) |= (1 << pin) )
/* Set bit P1.0 to be output Direction */
SET_PORT_PIN_DIR( P1, PIN0 );

## Slide 26: Port Macros [S8c]
#define SET_PORT_PIN_DIR (port, pin) ( (port)->DIR) |= (1 << pin) )
/* Set bit P1.0 to be output Direction */
SET_PORT_PIN_DIR( P1, PIN0 );

## Slide 27: Port Macros [S8d]
#define SET_PORT_PIN_DIR (port, pin) ( (port)->DIR) |= (1 << pin) )
/* Set bit P1.0 to be output Direction */
SET_PORT_PIN_DIR( P1, PIN0 );
typedef struct {
__I uint8_t IN;
uint8_t RESERVED0;
__IO uint8_t OUT;
uint8_t RESERVED1;
__IO uint8_t DIR;
uint8_t RESERVED2;
__IO uint8_t REN;
uint8_t RESERVED3;
… /* More Registers */
} DIO_PORT_TYPE;
/* Define the PORT Constants and Types*/
#define PIN0 (0x0)
#define DIO_PORT1_ADDR ((uint32_t) 0x40004C00)
#define P1 ( (DIO_PORT_Type*)(DIO_PORT1_ADDR) )
Port Structure Overlay

## Slide 28: Port Macros [S8e]
#define SET_PORT_PIN_DIR (port, pin) ( (port)->DIR) |= (1 << pin) )
/* Set bit P1.0 to be output Direction */
SET_PORT_PIN_DIR( P1, PIN0 );
typedef struct {
__I uint8_t IN;
uint8_t RESERVED0;
__IO uint8_t OUT;
uint8_t RESERVED1;
__IO uint8_t DIR;
uint8_t RESERVED2;
__IO uint8_t REN;
uint8_t RESERVED3;
… /* More Registers */
} DIO_PORT_TYPE;
/* Define the PORT Constants and Types*/
#define PIN0 (0x0)
#define DIO_PORT1_ADDR ((uint32_t) 0x40004C00)
#define P1 ( (DIO_PORT_Type*)(DIO_PORT1_ADDR) )
Port Structure Overlay

## Slide 29: Bit Band Macros [S9b]
Bit Band Region allows for atomic reads/writes of single bits for first 1MB of SRAM and Peripheral Memory
Not all of the SRAM & Peripheral Memory has a bit-band alias
Memory Map
Code
SRAM
Peripherals
(unused)
System Specific
0x00000000
0xFFFFFFFF
0xE0000000
0xDFFFFFFF
0x60000000
0x5FFFFFFF
0x20000000
0x1FFFFFFF
0x40000000
0x3FFFFFFF
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved
Peripheral Region
Reserved
Peripheral Bit-Band Alias Region
Reserved

## Slide 30: Bit Band Macros [S9b]
#define TA0CTL_ADDR (0x40000000)
/* Bit Band Region is offset from Peripheral/SRAM */
#define BB_OFFSET (0x02000000)
/* Macro Function to Read Memory */
#define HWREG32(addr) (*((volatile uint32_t *)(addr)))
/* Bit Band Alias Offset Address */
#define BITBAND_ADDR(addr, bit) ( (addr & 0xF0000000) + BB_OFFSET + \
((addr & 0xFFFFF) << 5) + (bit << 2) )
/* Set bit 1 of TA0CTL Register */
HWREG32( BITBAND_ADDR(TA0CTL_ADDR, 1) );

## Slide 31: Bit Band Macros [S9c]
#define TA0CTL_ADDR (0x40000000)
/* Bit Band Region is offset from Peripheral/SRAM */
#define BB_OFFSET (0x02000000)
/* Macro Function to Read Memory */
#define HWREG32(addr) (*((volatile uint32_t *)(addr)))
/* Bit Band Alias Offset Address */
#define BITBAND_ADDR(addr, bit) ( (addr & 0xF0000000) + BB_OFFSET + \
((addr & 0xFFFFF) << 5) + (bit << 2) )
/* Set bit 1 of TA0CTL Register */
HWREG32( BITBAND_ADDR(TA0CTL_ADDR, 1) );

## Slide 32: Macro Problems [S10a]
Numerous Issues with Macro Functions
  No Type Checking
  Bug Introduction
  Complex / Confusing Layers of Macros Calling Macros
  Code Size and Duplication

## Slide 33: Macro Problems [S10b]
Numerous Issues with Macro Functions
  No Type Checking
  Bug Introduction
  Complex / Confusing Layers of Macros Calling Macros
  Code Size and Duplication
#define PERIPH_BASE ((uint32_t) 0x40000000)
#define DIO_BASE (PERIPH_BASE + 0x00004C00)
#define P1_BASE (DIO_BASE + 0x0000)
#define P1DIR_ADDR (P1BASE + 0x0004)
Must specify type explicitly
#define SQUARE(x) ((x)*(x))
uint32_t y = 2;
uint32_t Y_sqrd = ;
Y_sqrd = SQUARE(y++);
uint32_t y = 2;
uint32_t Y_sqrd = ;
Y_sqrd = ((y++)*(y++));
After Preprocessing
Undefined Operation
Before Preprocessing

## Slide 34: Macro Problems [S10c]
Numerous Issues with Macro Functions
  No Type Checking
  Bug Introduction
  Complex / Confusing Layers of Macros Calling Macros
  Code Size and Duplication
#define PERIPH_BASE ((uint32_t) 0x40000000)
#define DIO_BASE (PERIPH_BASE + 0x00004C00)
#define P1_BASE (DIO_BASE + 0x0000)
#define P1DIR_ADDR (P1BASE + 0x0004)
#define HWREG8(x) (*((volatile uint8_t *)(x)))
#define P1DIR (HWREG8(P1DIR_ADDR))

## Slide 35: Macro Problems [S10d]
Numerous Issues with Macro Functions
  No Type Checking
  Bug Introduction
  Complex / Confusing Layers of Macros Calling Macros
  Code Size and Duplication
The preprocess will search and replace any used macro!

## Slide 36: Specialized C Functions [S11]
Functions are excellent for encapsulating a specialized operation
Calling a traditional C-function can decrease performance due to calling convention overhead

## Slide 37: Specialized C Functions [S11b]
Functions are excellent for encapsulating a specialized operation
Calling a traditional C-function can decrease performance due to calling convention overhead
  Saving data to stack
  Creating local variables
  Branching
Need to reduce performance hit
__attribute__( ( always_inline ) ) static inline void __enable_irq(void)
{
__ASM volatile ("cpsie i" : : : "memory");
}

## Slide 38: Specialized C Functions [S11c]
Functions are excellent for encapsulating a specialized operation
Calling a traditional C-function can decrease performance due to calling convention overhead
  Saving data to stack
  Creating local variables
  Branching
Need to reduce performance hit
__attribute__( ( always_inline ) ) static inline void __enable_irq(void)
{
__ASM volatile ("cpsie i" : : : "memory");
}

## Slide 39: Inline Keyword [S12a]
Compiler Attributes can apply to functions
  Inline – Skips calling convention, copies function body into calling code
__attribute__ ((always_inline)) inline int32_t add( int32_t x, int32_t y ) {
return (x + y);
}
Inline keyword is a c99 Feature  Not supported in c89
always_inline is a GCC attribute  Not supported in other compilers

## Slide 40: Inline Keyword [S12b]
Compiler Attributes can apply to functions
  Inline – Skips calling convention, copies function body into calling code
__attribute__ ((always_inline)) inline int32_t add( int32_t x, int32_t y ) {
return (x + y);
}
Compiler might
ignore this
Compiler will
NOT ignore this
Inline keyword is a c99 Feature  Not supported in c89
always_inline is a GCC attribute  Not supported on other compilers

## Slide 41: Inline Keyword [S12c]
Compiler Attributes can apply to functions
  Inline – Skips calling convention, copies function body into calling code
__attribute__ ((always_inline)) inline int32_t add( int32_t x, int32_t y ) {
return (x + y);
}
Compiler might
ignore this
Compiler will
NOT ignore this
Bad for / Will not work for
  Recursive functions
  Variadic functions
  Long functions
Good for
  Small functions

## Slide 42: Static Keyword [S13a]
Static Keyword can apply to functions to create private access

## Slide 43: Static Keyword [S13b]
Static Keyword can apply to functions to create private access
  Function/Variable only visible to current file
__attribute__( ( always_inline ) ) static inline void __enable_irq(void)
{
__ASM volatile ("cpsie i" : : : "memory");
}
core_cm4.h

## Slide 44: Static Keyword [S13c]
Static Keyword can apply to functions to create private access
  Function/Variable only visible to current file
Combine Static and Inline to prevent integrating all code into calling function
  Linkage is internal to file
__attribute__( ( always_inline ) ) static inline void __enable_irq(void)
{
__ASM volatile ("cpsie i" : : : "memory");
}
core_cm4.h

## Slide 45: Interface Library for GPIO [S14a]
GPIO Hardware
IO.c
IO_Read()
IO_Write()
IO_Configure()
Peripheral & Hardware Layer
Bare-Metal
Firmware
High Level Software – blink_LEDs.c
LED
LED
LED
LED
External Hardware
Application

## Slide 46: Interface Library for GPIO [S14b]
#include <stdio.h>
#include “msp.h”
__attribute__( ( always_inline ) ) static inline void IO_Read(DIO_PORT_Type * port,
uint8_t pin)
{
return ( ((port)->IN) & (1 << pin) );
}
__attribute__( ( always_inline ) ) static inline void IO_Write(DIO_PORT_Type * port,
uint8_t pin,
uint8_t value)
{
value ? ( ((port)->OUT) |= (1 << pin) ) : ( ((port)->OUT) &= ~(1 << pin) ) ;
}
IO_MSP432.h

## Slide 47: Interface Library for GPIO [S14c]
#include <stdio.h>
#include “msp.h”
__attribute__( ( always_inline ) ) static inline void IO_Read(DIO_PORT_Type * port,
uint8_t pin)
{
return ( ((port)->IN) & (1 << pin) );
}
__attribute__( ( always_inline ) ) static inline void IO_Write(DIO_PORT_Type * port,
uint8_t pin,
uint8_t value)
{
value ? ( ((port)->OUT) |= (1 << pin) ) : ( ((port)->OUT) &= ~(1 << pin) ) ;
}
IO_MSP432.h
KL25z
GPIO Hardware
IO_KL25Z.h
platform.c/.h
MKL25Z.h
blink_LEDs.c
MSP432
GPIO Hardware
IO_MSP432.h
platform.c/.h
msp432p401r.h
blink_LEDs.c

## Slide 48: Interface Library for GPIO [S14c]
#if defined (KL25Z ) && ! defined (MSP432)
#include “IO_KL25Z.h”
#elif defined (MSP432) && ! defined (KL25Z)
#include “IO_MSP432.h”
#else
#error “Platform not properly specified”
#endif
Platform.h
KL25z
GPIO Hardware
IO_KL25Z.h
platform.c/.h
MKL25Z.h
blink_LEDs.c
MSP432
GPIO Hardware
IO_MSP432.h
platform.c/.h
msp432p401r.h
blink_LEDs.c
$ make all PLATFORM=MSP432