## Slide 1: Advanced Pointer Use
Embedded Software Essentials
C2 M2 V5

## Slide 2: Advanced Pointers [S2]
Memories of an Embedded System
  Generic Pointer (void)
  Double Pointer
  Restrict Pointer
void * ptr1 = NULL;
void ** ptr2 = &ptr1;
uint32_t * restrict ptr3;
uint32_t ** ptr4;
sizeof( uint8_t* ) = sizeof( void* )
= sizeof( void** )
= sizeof( uint32_t** )
= sizeof( uint32_t* restrict )
= 32-Bits!1
sizeof( ptr1 ) = sizeof( ptr2 )
= sizeof( ptr3 )
= sizeof( ptr4 )
= 32-Bits! 1
1On our 32-bit ARM Architecture

## Slide 3: Void Pointer [S3a]
Void pointers are Generic Pointers, they point to a memory address
  void = Lack of type, dereferencing does not make sense!
1On our 32-bit ARM Architecture

## Slide 4: Void Pointer [S3b]
Void pointers are Generic Pointers, they point to a memory address
  void = Lack of type, dereferencing does not make sense!
Void Pointers are NOT NULL Pointers, but a NULL Pointer is a Void Pointer:
#define NULL (void*(0))
void * ptr1 = NULL;
sizeof( void* ) = sizeof( uint8_t* )
= sizeof( float* )
= sizeof( uint32_t* )
= 32-Bits!1
1On our 32-bit ARM Architecture

## Slide 5: Void Pointer [S3c]
Void pointers are Generic Pointers, they point to a memory address
  void = Lack of type, dereferencing does not make sense!
Must cast before using
No dereferencing on a void *
No pointer arithmetic on a void *
Void Pointers are NOT NULL Pointers, but a NULL Pointer is a Void Pointer:
#define NULL (void*(0))
void * ptr1 = NULL;
sizeof( void* ) = sizeof( uint8_t* )
= sizeof( float* )
= sizeof( uint32_t* )
= 32-Bits!1
1On our 32-bit ARM Architecture
void * ptr1 = (void*)0x40000000;
*((uint16_t*)ptr1) = 0x0202;
Equivalent to:
TA0CTL = 0x0202;

## Slide 6: Malloc and Void *[S4]
Malloc reserves blocks of data, it does not care how it is used
  Returns a void pointer, you cast this pointer for the intended use
8 Bytes
End
ptr
Heap States
After Malloc
Before Malloc
Start
char * ptr;
ptr = (char *)malloc(8*sizeof(char));
if (ptr == NULL) {
/* Allocation Failed!!! */
/* …Handle Failure */
}
/* Other Code */
free((void *)ptr);

## Slide 7: Void Pointer Example [S5a]
You might not know the underlying type without some processing
  Sequence of bytes being sent, first byte is type indicator
Microcontroller
GPIO
Flash
CPU-1
Peripheral
SRAM
UART
Microcontroller
GPIO
Flash
CPU-2
Peripheral
SRAM
UART
Platform 1
Platform 2

## Slide 8: Void Pointer Example [S5b]
You might not know the underlying type without some processing
  Sequence of bytes being sent, first byte is type indicator
Microcontroller
GPIO
Flash
CPU-1
Peripheral
SRAM
UART
Microcontroller
GPIO
Flash
CPU-2
Peripheral
SRAM
UART
Two embedded systems sending command and responses to each other
Platform 1
Platform 2

## Slide 9: Void Pointer Example [S5c]
You might not know the underlying type without some processing
  Sequence of bytes being sent, first byte is type indicator
Microcontroller
GPIO
Flash
CPU-1
Peripheral
SRAM
UART
Microcontroller
GPIO
Flash
CPU-2
Peripheral
SRAM
UART
Two embedded systems sending command and responses to each other
Platform 1
Platform 2
typedef enum {
RSP_TYPE_1 = 0,
RSP_TYPE_2 = 1,
} RSP_e;
typedef struct {
RSP_e rsp_type;
uint8_t data[4];
} rsp1;
typedef struct {
RSP_e rsp_type;
uint32_t data;
} rsp2;
Notes: Should there be a semicolon after RPS_TYPE_1 = 0 and after RPS_TYPE_2 = 1 ?

## Slide 10: Void Pointer Example [S5d]
You might not know the underlying type without some processing
  Sequence of bytes being sent, first byte is type indicator
typedef enum {
RSP_TYPE_1 = 0,
RSP_TYPE_2 = 1,
} RSP_e;
typedef struct {
RSP_e rsp_type;
uint8_t data[4];
} rsp1;
typedef struct {
RSP_e rsp_type;
uint32_t data;
} rsp2;
rsp1
Assume Packed: sizeof( rsp1 ) = sizeof( rsp2 ) = 8 Bytes to transmit
Data[3] | Data[2] | Data[1] | Data[0] | RSP_e = RSP_TYPE_1
Data | RSP_e = RSP_TYPE_2
rsp2
Microcontroller
GPIO
Flash
CPU-1
Peripheral
SRAM
UART
Platform 1
Microcontroller
GPIO
Flash
CPU-2
Peripheral
SRAM
UART
Platform 2
rsp2
First Word tells you how to interpret data fields
Notes: Should there be a semicolon after RPS_TYPE_1 = 0 and after RPS_TYPE_2 = 1 ?

## Slide 11: Double Pointer [S6a]
Double pointers are a pointer to a pointer
Must use the ** in declarations
sizeof( float** ) = sizeof( uint8_t** )
= sizeof( void** )
= sizeof( uint32_t** )
= 32-Bits!1
1On our 32-bit ARM Architecture
uint32_t var = 0x1234ABCD;
uint32_t * ptr3 = &var;
uint32_t ** ptr4 = &ptr3;

## Slide 12: Double Pointer [S6b]
Double pointers are a pointer to a pointer
Must use the ** in declarations
Used to set value of a pointer (address)
  Single dereference accesses pointer address
  Double dereference accesses pointer data
sizeof( float** ) = sizeof( uint8_t** )
= sizeof( void** )
= sizeof( uint32_t** )
= 32-Bits!1
1On our 32-bit ARM Architecture
uint32_t var = 0x1234ABCD;
uint32_t * ptr3 = &var;
uint32_t ** ptr4 = &ptr3;

## Slide 13: Double Pointer [S6c]
Double pointers are a pointer to a pointer
Must use the ** in declarations
Used to set value of a pointer (address)
  Single dereference accesses pointer address
  Double dereference accesses pointer data
sizeof( float** ) = sizeof( uint8_t** )
= sizeof( void** )
= sizeof( uint32_t** )
= 32-Bits!1
1On our 32-bit ARM Architecture
uint32_t var = 0x1234ABCD;
uint32_t * ptr3 = &var;
uint32_t ** ptr4 = &ptr3;
Memory
0x00
0x04
0x01
0x02
0x03
0x05
CD
AB
34
12
..
..
ptr3
var
0x00000000
ptr4 = &ptr3
&ptr3

## Slide 14: Double Pointer Example [S7]
Copies of pointers are made when passed into a function
  Original pointer address cannot be altered!
int8_t create_rsp1 (rsp1 ** r_p){
*r_p = (rsp1 *)malloc(sizeof(rsp1));
if (*r_p == NULL) {
/* Allocation Failed!!! */
return -1;
}
(*r_p)->rsp_type = RSP_TYPE_1;
return 0;
}
typedef enum {
RSP_TYPE_1 = 0,
RSP_TYPE_2 = 1,
} RSP_e;
typedef struct {
RSP_e rsp_type;
uint8_t data[4];
} rsp1;

## Slide 15: Restrict Qualified Pointer [S8a]
Restrict type qualifier helps compiler to optimize memory interactions
  Must use the restrict qualifier AFTER the * in declarations
Introduced in C99 Standard
sizeof( float* ) = sizeof( uint8_t* )
= sizeof( void* )
= sizeof( uint32_t* restrict )
= 32-Bits!1
1On our 32-bit ARM Architecture
uint32_t * restrict ptr4;

## Slide 16: Restrict Qualified Pointer [S8b]
Restrict type qualifier helps compiler to optimize memory interactions
  Must use the restrict qualifier AFTER the * in declarations
Only the data at this location or data near is accessed by this pointer
Largest speedup comes from iterative memory interaction
  Compiler removes unneeded assembly instructions
  Couple assembly instructions per loop
1On our 32-bit ARM Architecture
uint32_t * restrict ptr4;