## Slide 1: Function Pointers
Embedded Software Essentials
C2 M2 V6

## Slide 2: Function Pointers [S1a]
Pointer that points to functions
Defined just like a function
  Return type
  Function parameters
  Pointer name
void (* foo)();
int8_t void (* bar)( int8_t a, int8_t * b );
uint32_t (* func)( uint8_t param );
sizeof( ( void (*)) ) = sizeof( void* )
= sizeof( uint32_t* )
= 32-Bits!1
1On our 32-bit ARM Architecture
Example Declarations

## Slide 3: Function Pointers [S1a]
Pointer that points to functions
Defined just like a function
  Return type
  Function parameters
  Pointer name
Dereferencing a function pointer will call a function
void (* foo)();
int8_t void (* bar)( int8_t a, int8_t * b );
uint32_t (* func)( uint8_t param );
sizeof( void (*foo) ) = sizeof( void* )
= sizeof( uint32_t* )
= 32-Bits!1
1On our 32-bit ARM Architecture
Example Declarations
(* foo)(); or foo();

## Slide 4: Function Pointer Syntax [S2a]
Declaration requires parentheses and a pointer *
<type> (* <function_pointer_name>)(<parameter list>) = <function-address>;
Must be inside parentheses

## Slide 5: Function Pointer Syntax [S2b]
Declaration requires parentheses and a pointer *
<type> (* <function_pointer_name>)(<parameter list>) = <function-address>;
int8_t * foo();
Must be inside parentheses
int8_t (* foo)();
A function pointer variable declaration that returns a int8_t type
A function declaration that returns a int8_t pointer type
/* Function Bar Prototype */
int8_t bar();
/* Function Pointer */
int8_t (* foo)() = &bar;

## Slide 6: Function Pointer Syntax [S3a]
Initialization and assignment to a function pointer should have matching return types and parameter list
<type> (* <function_pointer_name>)(<parameter list>) = <function-address>;
int foo( int a, int b );
ret = foo(1, 3)
int (* fptr)( int c, int d );
fptr = &foo;
ret = fptr(1, 3);
Declarations:
Should be consistent with function being assigned
Calling the functions:

## Slide 7: Function Pointer Syntax [S3b]
Initialization and assignment to a function pointer should have matching return types and parameter list
<type> (* <function_pointer_name>)(<parameter list>) = <function-address>;
int foo( int a, int b );
int bar( int c, int d );
typedef int (* fptr_TYPE)( int c, int d );
Two function pointer declarations:
Calling the functions:
fptr_TYPE fptr1 = &foo;
fptr_TYPE fptr2 = &bar;
ret = fptr1(1, 3);
ret = (*fptr2)(4, 5);
Defined functions:

## Slide 8: Function Pointer Array [S4a]
Function pointers can be declared with an array
typedef void (* FuncPtr_t[2])();
FuncPtr_t example =
{
foo,
bar
};
Alternatively…
typedef void (* FuncPtr_t());
FuncPtr_t example[2] =
{
foo,
bar
};

## Slide 9: Function Pointer Array [S4b]
Function pointers can be declared with an array
typedef void (* FuncPtr_t[2])();
FuncPtr_t example =
{
foo,
bar
};
typedef enum
{
FP_FOO = 0,
FP_BAR = 1,
} FP_e;
example[FP_FOO]();
example[FP_BAR]();
Example Calls:

## Slide 10: Interrupt Vector Table [S5a]
Interrupts are special events that request the CPU to perform a specific operation
Code Memory
0x0
.text
.intvecs
.const
(unused)
.cinit
.pinit

## Slide 11: Interrupt Vector Table [S5b]
Interrupts are special events that request the CPU to perform a specific operation
  E.g. Timers, GPIO, CPU Exception
Interrupt Service Routine (ISR): Function to be called in response to an interrupt request
Code Memory
0x0
.text
.intvecs
.const
(unused)
.cinit
.pinit
Interrupt Vectors
Stack Pointer
NMI
Hard Fault
MPU Fault
Bus Fault
…
Power Control
Watchdog
FPU
…

## Slide 12: Interrupt Vector Table [S5c]
Interrupts are special events that request the CPU to perform a specific operation
  E.g. Timers, GPIO, CPU Exception
Interrupt Service Routine (ISR): Function to be called in response to an interrupt request
Placed at address 0x0 in code memory
Code Memory
0x0
.text
.intvecs
.const
(unused)
.cinit
.pinit
Interrupt Vectors
Stack Pointer
NMI
Hard Fault
MPU Fault
Bus Fault
…
Power Control
Watchdog
FPU
…
Array of function addresses

## Slide 13: Vector Table [S6a]
Definition requires both linker mapping and C/assembly code
#pragma DATA_SECTION(interruptVectors, ".intvecs")
void (* const interruptVectors[])(void) =
{
(void (*)(void))((uint32_t)&__STACK_END), /* Initial stack pointer */
reset_ISR, /* Reset handler */
nmi_ISR, /* NMI handler */
fault_ISR, /* Hard fault handler */
mpu_ISR, /* MPU fault handler */
busfault_ISR, /* Bus fault handler */
… /* More Interrupt handlers */
SECTIONS
{
.intvecs : > 0x00000000
.text : > MAIN
.const : > MAIN
…
Linker Script Excerpt
MSP432 Startup File Excerpt

## Slide 14: Vector Table [S6b]
Definition requires both linker mapping and C/assembly code
#pragma DATA_SECTION(interruptVectors, ".intvecs")
void (* const interruptVectors[])(void) =
{
(void (*)(void))((uint32_t)&__STACK_END), /* Initial stack pointer */
reset_ISR, /* Reset handler */
nmi_ISR,, /* NMI handler */
fault_ISR, /* Hard fault handler */
mpu_ISR, /* MPU fault handler */
busfault_ISR, /* Bus fault handler */
… /* More Interrupt handlers */
SECTIONS
{
.intvecs : > 0x00000000
.text : > MAIN
.const : > MAIN
…
Linker Script Excerpt
MSP432 Startup File Excerpt

## Slide 15: Vector Table [S7a]
Vector table is an array of function addresses
  Used to “jump” into a routine when interrupt occurs
#pragma DATA_SECTION(interruptVectors, ".intvecs")
void (* const interruptVectors[])(void) =
{
(void (*)(void))((uint32_t)&__STACK_END),
reset_ISR,
nmi_ISR,
fault_ISR,
mpu_ISR,
busfault_ISR,
… /* More Interrupt handlers */
MSP432 Startup File Excerpt

## Slide 16: Vector Table [S7b]
Vector table is an array of function addresses
  Used to “jump” into a routine when interrupt occurs
#pragma DATA_SECTION(interruptVectors, ".intvecs")
void (* const interruptVectors[])(void) =
{
(void (*)(void))((uint32_t)&__STACK_END),
reset_ISR,
nmi_ISR,
fault_ISR,
mpu_ISR,
busfault_ISR,
… /* More Interrupt handlers */
MSP432 Startup File Excerpt
Function pointer declaration
All Interrupt Subroutines are type void functions

## Slide 17: Vector Table [S7c]
Vector table is an array of function addresses
  Used to “jump” into a routine when interrupt occurs
#pragma DATA_SECTION(interruptVectors, ".intvecs")
void (* const interruptVectors[])(void) =
{
(void (*)(void))((uint32_t)&__STACK_END),
reset_ISR,
nmi_ISR,
fault_ISR,
mpu_ISR,
busfault_ISR,
… /* More Interrupt handlers */
MSP432 Startup File Excerpt
Array should be read only functions set at compile

## Slide 18: Vector Table [S8a]
Vector table is an array of function addresses
  Used to “jump” into a routine when interrupt occurs
#pragma DATA_SECTION(interruptVectors, ".intvecs")
void (* const interruptVectors[])(void) =
{
(void (*)(void))((uint32_t)&__STACK_END),
reset_ISR,
nmi_ISR,
fault_ISR,
mpu_ISR,
busfault_ISR,
… /* More Interrupt handlers */
MSP432 Startup File Excerpt
First element is the initial stack pointer to initialize the Core CPU Registers
High Priority ARM Core Exceptions